## Slide 1: QuantSparse 3D Biweekly 2026-01-15
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  Ventaglio – Fixes, performance analysis, and backend
  3D System – Adapting SoftHier system & SW stack to 3D
Timeline
Discussion

## Slide 3: Ventaglio Backend Analysis
Performed the backend implementation with GF12 FinFET
VTL_v0.1 design
  Introduced a new critical timing path, adding ~0.1 ns delay under the SS corner
  Root cause: the index datapath  Upon receiving a new request, indices are loaded into VTL and used for the gather operation in the same cycle
  Solution: Implemented an index preloading mechanism, triggered with two cases:
    When an index is written to the VRF by a valid VLX instruction
    When the current index stored in the VTL is depleted.
  Indices are available ahead of gather/scatter operations, eliminating the extra delay

## Slide 4: Ventaglio Backend Analysis
Performed the backend implementation with GF12 FinFET
VTL_v0.2 design
  Timing issue is resolved, and Ventaglio no longer introduces a new critical timing path
  Area impact:
    Integrating Ventaglio increases the area by 55.9 kGE in GF12, ~5% at the Spatz core level. (4 channels, 4 rows)
    ~85% of the area increment is from memory units in VTL
    Compared to the alternative approach of doubling VRF banks, Ventaglio
      Incurs lower area overhead
      Providing greater flexibility and programmability

## Slide 5: Ventaglio Performance Analysis
Datapath behavior under an SpMV workload (Gustavson’s dataflow).
Ideal waveform
  Should be only one cycle latency between consecutive vfxmacc operation (unavoidable in current design)
  Comes from loading indices from L1 into the VRF
  Weight matrix is not reused under SpMV workload  VLSU bandwidth matches that of the VPU
  Theoretical maximum VPU utilization is 94.1% (LMUL=8).
VTL_v0.2 design
  Two additional stall cycles are observed
  Root cause: VLSU behavior when two load instructions arrive back-to-back. VLSU requires a transition cycle to commit the previous instruction

## Slide 6: Ventaglio Performance Analysis
Datapath behavior under an SpMV workload (Gustavson’s dataflow).
VTL_v0.3 design: Ongoing optimization
  These two extra cycles can be removed by modifying the VLSU commit logic
  Current progress: Additional cycles are removed while memory requests may commit improperly in some corner cases. Fix in progress

## Slide 7: Ventaglio: Next Steps
Features:
  [HW] Loop unrolling support
  [HW] More N:M formats  cost estimation
  [HW/SW] Duo-level ELLPACK format support
  [SW] VTL GVSoC model
Upcoming projects:
  Ventaglio + MX datapath in Spatz
  Ventaglio + RVV matrix extension in Spatz

## Slide 8: 3D System: Extending SoftHier Model
Completed 3D NoC integration in SoftHier
Adapted GVSoC system model
  Logic dies (clusters) stacked in 3D mesh
  Adapted outstanding requests to account for higher distances (Nx + Ny  Nx + Ny + Nz)
  HBM controllers remain in base die for now
  Transparent HW extension through additional system parameter
Extended cluster registers
  Provide Z coordinate and 3D cluster ID
  Extend inter-cluster mesh barrier to 3D
HBM
HBM
HBM
HBM
HBM
HBM
HBM
HBM
HBM

## Slide 9: 3D System: Extending SoftHier Runtime
Extended Runtime for 3D mesh
  New methods for own ID & Z neighbors
  Extended global & mesh barriers
  Working on mesh DMA primitives
First debugging of 3D mesh execution
  Upper clusters can fetch and run code from HBM
  Currently: debugging 3D barriers for upper cores

## Slide 10: 3D System: Next Steps
Software:
  Resolve barrier issues
  Demonstrate DMA primitives in 3D
  Demonstrate compute kernels on 3D mesh
Hardware:
  Make Z links parametric (throughput, arity)
  Explore different Z topologies