## Slide 1: QuantSparse 3D Biweekly 2026-06-11
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch
Chi Zhang chizhang@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  3D System – 3D GEMV Benchmarks
  TileLang – Methodology and progress update
Timeline
Discussion

## Slide 3: 3D stack DRAM-on-logic
Cluster
R
Cluster
R
Cluster
R
Cluster
R
Cluster
R
Cluster
R
Cluster
R
Cluster
R
Cluster
R
Cluster
R
Cluster
R
Cluster
R
Cluster
R
Cluster
R
Cluster
R
Cluster
R
3D-stack DRAM
TSV
logic
We already modeled by extending SoftHier
  For Each Cluster add arbiters to:
  1. DRAM channels on top
  2. NoC Routers in the logic die
Core 0
Core 0
…
Core n
Matrix
Engine
DMA
I $
L1 local memory
Vector
Engine
Interconnect
To DATA NoC Router
To SYNC NoC Router
TE Cluster
NoC Router
DRAM.ch CTRL

## Slide 4: Benchmark 3D GEMV
Simple GEMV dataflow for 3D-DRAM arch
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
2. Cluster-wise local GEMV
x
=
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
cluster
1.Row-wise Multicast
3. Col-wise Reduce

## Slide 5: Benchmark 3D GEMV
Benchmark on different arch scales
3D_2x2
3D-DRAM BW = 0.25TB/s
3D_4x4
3D-DRAM BW = 1TB/s
3D_8x8
3D-DRAM BW = 4TB/s
3D_16x16
3D-DRAM BW = 16TB/s
3D_32x32
3D-DRAM BW = 64TB/s

## Slide 6: Benchmark 3D GEMV
Benchmark FP8 GEMV 4096x16384
  Tile size = 128x256
  Scale out -> Fewer data per channel -> hard to amortize double-buffer pipeline latency
  We need smarter & fine-grain dataflow design
Chart: Bandwidth TB/s
| 3D_2x2 | 3D_4x4 | 3D_8x8 | 3D_16x16 | 3D_32x32
Reached DRAM BW (TB/s) | 0.20811 | 0.8414 | 3.2023 | 10.084 | 19.6628
Max DRAM BW (TB/s) | 0.25 | 1 | 4 | 16 | 64
DRAM BW Uti | 0.83243 | 0.8414 | 0.80059 | 0.63025 | 0.30723

## Slide 7
Motivation: Lifting the Programming Abstraction for Scalable Systems
Hardware scales for scaling of ML workloads
  ML system scale-out with heterogeneity and additional hierarchy  scaling programming complexity
To program:
  Threads as the abstraction unit for programming  Too many hardware details and primitives to consider
Do programmers have an easier-to-use abstraction that balances performance and productivity?

## Slide 8
Programmer hand-codes on tiles:
Dataflow
Memory management
programmer expresses where data lives and what to compute; compiler decides how and when
Tile as an abstraction level
  Designed for NVIDIA GPU
  TVM as the backbone for code transformation and code generation
TileLang: Tile-based Domain-Specific Language
github: tile-ai/tilelang
@tilelang.jit
def matmul(A, B, C, M, N, K, block_M, block_N, block_K):
CONFIGURE PHYSICAL COMPUTE UNIT (grid, block config in GPU)
with T.Kernel(ceildiv(N,block_N), ceildiv(M,block_M)) as (bx, by):
DECLARE BUFFERS
A_shared = T.alloc_shared((block_M, block_K), dtype)
B_shared = T.alloc_shared((block_K, block_N), dtype)
C_local = T.alloc_fragment((block_M, block_N), dtype);
T.clear(C_local)
REDUCE OVER K — pipelining with double-buffering
for ko in T.Pipelined(ceildiv(K, block_K), num_stages=2):
TILE LOAD
T.copy(A[by*block_M, ko*block_K], A_shared)
T.copy(B[ko*block_K, bx*block_N], B_shared)
COMPUTE
T.gemm(A_shared, B_shared, C_local)
TILE STORE
T.copy(C_local, C[by*block_M, bx*block_N])
Tilelang programming example: GEMM
Introducing TileLang to SoftHier, two missing components:
  Collective communication primitives
  Explicit cluster-level execution bindings

## Slide 9
Deeploy
Lowers ONNX operator graphs to C
Allows customized optimization passes
Graph IR frontend
Tilelang DSL
Tile-level abstraction for programmer
Deeploy: Bring Automation to Code Transformation
Allows customized dataflow definition
Targets GPU
A Programming Model
A Compiler for Code Generation

## Slide 10
@tilelang.jit
def summa_gemm(A, B, C, M, K, N,
BM, BN, BK: int, SX, SY: int, GX, GY: int):
// In this example, SX=GX, SY=GY (1 Group per System)
with T.Kernel(T.ceildiv(M,GY*BM), T.ceildiv(N,GX*BN)) as (by, bx):
with T.cluster_group("summa", x=GX, y=GY, axes=("x", "y")) as (inst_id, local_x, local_y):
A_local = T.alloc_l1((BM, BK), dtype)
B_local = T.alloc_l1((BK, BN), dtype)
C_local = T.alloc_l1((BM, BN), dtype)
T.clear(C_local)
for bk in T.Pipelined(T.ceildiv(K, BK), num_stages=2):
if local_x == local_y:
T.copy(A[(by * GY + local_y) * BM, bk * BK], A_local)
T.copy(B[bk * BK, (bx * GX + local_x) * BN], B_local)
T.broadcast(A_local, level="intra_group", axis="x",
group="summa", root=local_y)
T.broadcast(B_local, level="intra_group", axis="y",
group="summa", root=local_x)
T.gemm(A_local, B_local, C_local, clear_accum=False)
T.copy(C_local, C[(by*GY+local_y)*BM, (bx*GX+local_x)*BN])
DSL: Extension on TileLang
To support tile-based many-PE architecture:
Explicit binding of work with physical cluster, accelerator units
Explicit memory allocation at local TCDM or HBM
Explicit communication between clusters
Explicit synchronization at different scopes

## Slide 11
@tilelang.jit
def summa_gemm(A, B, C, M, K, N,
BM, BN, BK: int, SX, SY: int, GX, GY: int):
// In this example, SX=GX, SY=GY (1 Group per System)
with T.Kernel(T.ceildiv(M,GY*BM), T.ceildiv(N,GX*BN)) as (by, bx):
with T.cluster_group("summa", x=GX, y=GY, axes=("x", "y")) as (inst_id, local_x, local_y):
A_local = T.alloc_l1((BM, BK), dtype)
B_local = T.alloc_l1((BK, BN), dtype)
C_local = T.alloc_l1((BM, BN), dtype)
T.clear(C_local)
for bk in T.Pipelined(T.ceildiv(K, BK), num_stages=2):
if local_x == local_y:
T.copy(A[(by * GY + local_y) * BM, bk * BK], A_local)
T.copy(B[bk * BK, (bx * GX + local_x) * BN], B_local)
T.broadcast(A_local, level="intra_group", axis="x",
group="summa", root=local_y)
T.broadcast(B_local, level="intra_group", axis="y",
group="summa", root=local_x)
T.gemm(A_local, B_local, C_local, clear_accum=False)
T.copy(C_local, C[(by*GY+local_y)*BM, (bx*GX+local_x)*BN])
DSL: Extension on TileLang
To support tile-based many-PE architecture:
Explicit binding of work with physical cluster, accelerator units
Explicit memory allocation at local TCDM or HBM
Explicit communication between clusters
Explicit synchronization at different scopes
For simplicity, what are added and exposed to programmer:
Schedule:
Hierarchical schedule T.cluster_group
with axis annotation and spatial cluster id
A scheduling scope higher than single cluster tile, lower than entire chip
Communication:
Collective communication T.broadcast, T.reduce
Simplify communication patterns for programmers
Reuse Tilelang parser to generate Tilelang Abstract Syntax Tree (AST)
Others handled by compiler

## Slide 12
Compiler: what the compiler decides
T.cluster_group("tp", x=4, y=1,num_groups=4,
axes=("x","y")) as (gid,local_x, local_y)
User Writes
Compiler Decides
Topology
Logical cluster groups → physical clusters
[0,1,2,3] [4,5,6,7] [8,9,10,11] [12,13,14,15]
Logical axes, id recorded
with T.cluster_group(…) as (gid,local_x, local_y):
T.broadcast(A_local, axis="x", level=“intra_group", root=local_y)
Collectives
row_mask = 0x3 col_mask = 0xF
If (cluster_id == local_y) {
flex_dma_async_broadcast(...,
row_mask, col_mask, ...);
}
for bk in T.Pipelined(K//BK, num_stages=2):
T.copy(A → A_local)
T.gemm(A_local, B_local, C_local)
Pipelining
for i in T.Parallel(chunk):
x[i] = T.sigmoid(x[i])
Vectorization
work split: per-core SID, strided base addr stripmine: vsetvli loop over hardware VLEN op decomp: sigmoid → vfmul·vfexp·vfdiv·vfadd·vfdiv emission: inline RISC-V V asm for Spatz Engine

## Slide 13
Kernel: 2D SUMMA GEMM
Numerical verification against a bit-true golden:
Reference: RedMule's exact FP16 FMA in software.
Verified with different input shapes.
@tilelang.jit
def summa_gemm(A, B, C, M, K, N,
BM: int, BN: int, BK: int, GX: int, GY: int):
with T.Kernel(T.ceildiv(M,GY*BM), T.ceildiv(N,GX*BN)) as (by, bx):
with T.cluster_group("summa", x=GX, y=GY, num_groups=1,
axes=("x", "y")) as (inst_id, local_x, local_y):
A_local = T.alloc_fragment((BM, BK), dtype)
B_local = T.alloc_fragment((BK, BN), dtype)
C_local = T.alloc_fragment((BM, BN), dtype)
T.clear(C_local)
for bk in T.Pipelined(T.ceildiv(K, BK), num_stages=2):
if local_x == local_y:
T.copy(A[(by * GY + local_y) * BM, bk * BK], A_local)
T.copy(B[bk * BK, (bx * GX + local_x) * BN], B_local)
T.broadcast(A_local, level="intra_group", axis="x",
group="summa", root=local_y)
T.broadcast(B_local, level="intra_group", axis="y",
group="summa", root=local_x)
T.gemm(A_local, B_local, C_local, clear_accum=False)
T.copy(C_local, C[(by*GY+local_y)*BM, (bx*GX+local_x)*BN])

## Slide 14
Kernel: 2D SUMMA GEMM
Numerical verification against a bit-true golden:
Reference: RedMule's exact FP16 FMA in software.
Verified with different input shapes.
@tilelang.jit
def summa_gemm(A, B, C, M, K, N,
BM: int, BN: int, BK: int, GX: int, GY: int):
with T.Kernel(T.ceildiv(M,GY*BM), T.ceildiv(N,GX*BN)) as (by, bx):
with T.cluster_group("summa", x=GX, y=GY, num_groups=1,
axes=("x", "y")) as (inst_id, local_x, local_y):
A_local = T.alloc_fragment((BM, BK), dtype)
B_local = T.alloc_fragment((BK, BN), dtype)
C_local = T.alloc_fragment((BM, BN), dtype)
T.clear(C_local)
for bk in T.Pipelined(T.ceildiv(K, BK), num_stages=2):
if local_x == local_y:
T.copy(A[(by * GY + local_y) * BM, bk * BK], A_local)
T.copy(B[bk * BK, (bx * GX + local_x) * BN], B_local)
T.broadcast(A_local, level="intra_group", axis="x",
group="summa", root=local_y)
T.broadcast(B_local, level="intra_group", axis="y",
group="summa", root=local_x)
T.gemm(A_local, B_local, C_local, clear_accum=False)
T.copy(C_local, C[(by*GY+local_y)*BM, (bx*GX+local_x)*BN])

## Slide 15
Kernel: 2D SUMMA GEMM
Numerical verification against a bit-true golden:
Reference: RedMule's exact FP16 FMA in software.
Verified with different input shapes.
@tilelang.jit
def summa_gemm(A, B, C, M, K, N,
BM: int, BN: int, BK: int, GX: int, GY: int):
with T.Kernel(T.ceildiv(M,GY*BM), T.ceildiv(N,GX*BN)) as (by, bx):
with T.cluster_group("summa", x=GX, y=GY, num_groups=1,
axes=("x", "y")) as (inst_id, local_x, local_y):
A_local = T.alloc_fragment((BM, BK), dtype)
B_local = T.alloc_fragment((BK, BN), dtype)
C_local = T.alloc_fragment((BM, BN), dtype)
T.clear(C_local)
for bk in T.Pipelined(T.ceildiv(K, BK), num_stages=2):
if local_x == local_y:
T.copy(A[(by * GY + local_y) * BM, bk * BK], A_local)
T.copy(B[bk * BK, (bx * GX + local_x) * BN], B_local)
T.broadcast(A_local, level="intra_group", axis="x",
group="summa", root=local_y)
T.broadcast(B_local, level="intra_group", axis="y",
group="summa", root=local_x)
T.gemm(A_local, B_local, C_local, clear_accum=False)
T.copy(C_local, C[(by*GY+local_y)*BM, (bx*GX+local_x)*BN])

## Slide 16
Kernel: 2D SUMMA GEMM
Numerical verification against a bit-true golden:
Reference: RedMule's exact FP16 FMA in software.
Verified with different input shapes.
@tilelang.jit
def summa_gemm(A, B, C, M, K, N,
BM: int, BN: int, BK: int, GX: int, GY: int):
with T.Kernel(T.ceildiv(M,GY*BM), T.ceildiv(N,GX*BN)) as (by, bx):
with T.cluster_group("summa", x=GX, y=GY, num_groups=1,
axes=("x", "y")) as (inst_id, local_x, local_y):
A_local = T.alloc_fragment((BM, BK), dtype)
B_local = T.alloc_fragment((BK, BN), dtype)
C_local = T.alloc_fragment((BM, BN), dtype)
T.clear(C_local)
for bk in T.Pipelined(T.ceildiv(K, BK), num_stages=2):
if local_x == local_y:
T.copy(A[(by * GY + local_y) * BM, bk * BK], A_local)
T.copy(B[bk * BK, (bx * GX + local_x) * BN], B_local)
T.broadcast(A_local, level="intra_group", axis="x",
group="summa", root=local_y)
T.broadcast(B_local, level="intra_group", axis="y",
group="summa", root=local_x)
T.gemm(A_local, B_local, C_local, clear_accum=False)
T.copy(C_local, C[(by*GY+local_y)*BM, (bx*GX+local_x)*BN])

## Slide 17
Kernel: 2D SUMMA GEMM
GVSOC TRACE — 16 CLUSTERS · M, K, N = 512, 7168, 512
iDMA Transfer
RedMule compute

## Slide 18
Partitioning K dimension into different cluster_group
Suitable for flat GEMM with small M dimension (e.g. 512x7168x2048)
Kernel: SUMMA GEMM
with Split-K works easily

## Slide 19
Partitioning K dimension into different cluster_group
Suitable for flat GEMM with small M dimension (e.g. 512x7168x2048)
Kernel: SUMMA GEMM
with Split-K works easily
@tilelang.jit
def summa_gemm_split_k(A, B, C, M, K, N,
BM, BN, BK, SX, SY: int, GX, GY: int):
with T.Kernel(T.ceildiv(M,GY*BM), T.ceildiv(N,GX*BN)) as (by, bx):
with T.cluster_group("summa", x=GX, y=GY,
num_groups=(SX/GX)*(SY/GY),
axes=("x","y"), split_axes=("k0","k1"), split_shape=(GX, GY) ) as (inst_id, local_x, local_y, group_k0, group_k1):
# split K into different cluster groups
K_per_group = T.ceildiv(K, num_groups)
K_base = (group_k0*GX+group_GY)*K_per_group
for bk in T.Pipelined(T.ceildiv(K_per_group, BK), num_stages=2):
if local_x == local_y:
T.copy(A[(by * GY + local_y) * BM, K_base + bk * BK], A_local)
T.copy(B[K_base + bk * BK, (bx * GX + local_x) * BN], B_local)
T.broadcast(A_local, level="intra_group", axis="x",
group="summa", root=local_y)
T.broadcast(B_local, level="intra_group", axis="y",
group="summa", root=local_x)
T.gemm(A_local, B_local, C_local, clear_accum=False)
# reduce along k axis
T.reduce(C_local, op="sum", level="inter_group", axis="k0", group="summa")
T.reduce(C_local, op="sum", level="inter_group", axis="k1", group="summa")
# one cluster group copies back result
if inst_id == 0:
T.copy(C_local, C[(by*GY+local_y)*BM, (bx*GX+local_x)*BN])

## Slide 20
2D SUMMA GEMM: Tilelang DSL vs. Hand-Written C
TILELANG
20
lines of Tilelang code
HAND-WRITTEN C
523
lines of C
Both produce numerically correct C code
The 20 lines Tilelang code can control:
Tiling size, axis
Software pipeline
Collective communication strategy (axis, scope, root cluster)

## Slide 21
Experimental variables:
Cluster Config: 4x4 clusters
Tile sizes: BM = BN = BK = 128
2D SUMMA GEMM: Tilelang DSL vs. Hand-Written C
Kernels produced by compiler
have performance close to hand-written C

## Slide 22
Summary
DSL: Extension on Tilelang targeting general tile-based many-PE hardware architecture
Utilization:
  Macro kernels: simplified API, explicit dataflow control
  Complex layers: Able to describe FlashAttention, easy adaptation from TileLang kernel libraries
  Customized dataflow exploration: FlatAttention, 3D-FlatAttention
Current progress:
  Semester project finished, code-cleanup and open-source in progress