## Slide 1: QuantSparse 3D Biweekly 2026-06-25
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch
Chi Zhang chizhang@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  Sparsity handling in memory endpoints
  Ventaglio open-source release
Timeline
Discussion

## Slide 3: Handling Sparsity Beyond Core-level
We handle fine-grained element-wise sparsity at core-level
  Ventaglio for dual-sparsity at moderate-sparse regime
  Unstructured extreme-sparse regime support under-developed
What is missing
  In prefill stage:
    matrix-matrix multiplication dominant
    compute-bound, sparsity translate to end-to-end speedup
  In auto-regressive decoding stage
    vector-level tensor contraction
    memory-bound, efficient sparsity handling in memory endpoints
  Sparse attention, vector quantization induced codebook accesses
    Vector-level gather from memory endpoint

## Slide 4: Sparse Pattern Analysis
Sparse attention
  What to gather: KV cache entries
  How to gather: runtime generated indexing  core side generated
  Access granularity: head dimension (128~512 elements) in multiple-GiB range
VQ codebook access
  What to gather: codebook entries
  How to gather: compile-time determined indexing  memory stored
  Access granularity: 4-16 elements in multiple-MiB range

## Slide 5: Memory-side Controller Extension for Sparsity Handling
Key features
  Decoupled core request and data movement
  Semantic extension for native index handling
  Accept index streams from both core and memory side
  Narrow access coalescing

## Slide 6: AXI-Pack: Bus Packing for AXI4 Indirect Accesses
Target: memory-side index streams
Extends the request channels AR and AW with user signals to support packed irregular burst
  pack bit indicates whether extension is enabled
  index size and base offset for indirect bursts
Controller architecture
  Adapter translates both regular and irregular bursts to sequences of n parallel word accesses
  Adapter forwards requests to converters for concurrent burst handling
  index stage fetches indices from memory
  element stage uses these indices to fetch indirect elements and pack them into R beats
  requested elements packed by a beat packer as specified by metadata
Zhang, Chi, et al. "Axi-pack: Near-memory bus packing for bandwidth-efficient irregular workloads." 2023 Design, Automation & Test in Europe Conference & Exhibition (DATE). IEEE, 2023.

## Slide 7: Near-Memory Parallel Indexing and Coalescing
Target: Index + DRAM access granularity
Push AXI-Pack to modern DRAM backend: backing narrow irregular stream elements onto wide memory buses
Controller architecture
  element request generator produces N parallel narrow element requests based on the index stream
  N parallel requests pass to coalescer to form wide DRAM access
    Upsizer widen the request window
    Request watcher identifies accesses targeting at the same wide DRAM block
    Response splitter retrieves the parallel narrow elements from the wide downstream data response
Zhang, Chi, et al. "Near-memory parallel indexing and coalescing: Enabling highly efficient indirect access for SpMV." 2024 Design, Automation & Test in Europe Conference & Exhibition (DATE). IEEE, 2024.

## Slide 8: Extending Controller for LLM Sparse Workload
Missing features
  Core-side index stream handling
  Granularity alignment
  Multi-node and memory endpoint exploration