## Slide 1: QuantSparse3D 2026-09-29 Bi-weekly
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch
Chi Zhang chizhang@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  Sparsity handling in memory endpoints, multi-node GVSoC model
Timeline
Discussion

## Slide 3: Recap: Sparse DMA in GVSoC
Calibration against the RTL model
Cycle count deviation within 10%
Worst cycle deviation: 8.80%
Worst DMA-window deviation: 8.94%
Original gather experiment
RTL
GVSoC
0
1,000
2,000
3,000
3099
3056
Core loop
1952
1914
Inlined loop
1236
1159
HW gather
Software-measured cycles • 128 gathered rows
Accuracy validated on the measured gather workloads.
Implementation
Sparse gather added to the GVSoC iDMA model
Indices select scattered source rows
DMA gathers rows into local memory

## Slide 4: Extending Sparse DMA to Multi-node System
Implementation
  Extended the iDMA engine in SoftHier with updated gather support
  Same modeling methodology as standalone iDMA
  Instantiated 4x4 clusters, 16 HBM nodes on all 4 edges
Sanity test
  Cluster 0 issues gather requests to HBM node 0
  Same workload:
    Top-k sparse attention gather access patterns
    128 entries with 256-byte each in a 2k context
  Same performance gain comparing with standalone iDMA modeling
3.10x

## Slide 5: Extending Sparse DMA to Multi-node System
Multi-node test setup
  4 x 4 clusters, one independent user context per cluster; 16 HBM nodes on all four edges
  Each cluster workload:
    Gather 128 KV entries out of 2k context, each is 128 x FP16 (32 KiB payload in total)
    System-wise 0.5 MiB read payload, from 4 MiB of non-overlapping context address space, fully interleaved in 16 HBM nodes
Benchmark Settings
  3 software implementations:
    Core-loop
    Inline-loop
    HW-gather with sparse DMA

## Slide 6: Visualizing NoC traffic
Baseline result analysis
  Core-loop implementation consistently shows less efficient gathering
  NoC traffic is far from being saturated, throughput is limited by DMA request issuing frequency, achieving avg. 212.43 GiB/s HBM throughput (23.07% HBM util.)
  Inline-loop implementation increased the NoC traffic through software optimizations, improved HBM throughput to 302.01 GiB/s (32.80% HBM util.)
  The improvement is aligned with the single-node benchmark
Core-loop
Inline-loop

## Slide 7: Visualizing NoC traffic
Sparse-DMA result analysis
  Increased the NoC traffic by offloading the request generation to DMA midend, achieving avg. 455.90 GiB/s HBM throughput (49.51% HBM util.)
  Achieved 2.14x improvement comparing with core-loop implementation
  Comparing with the single-node results, the HBM avg. utilization reduced from 63.8% to 49.5%
  Potential reasons:
    NoC request contention
    Larger gathering context reduced memory endpoint serving efficiency
2.14x
Next step:
  Impact of KV mapping and context range
  Serving mythology (e.g., all cluster serve the same user)

## Slide 8: Backup: Individual HBM Utilization Breakdown

## Slide 9: Backup: Core-Loop Read Request & Response Visualization

## Slide 10: Backup: Inline-Loop Read Request & Response Visualization

## Slide 11: Backup: HW-Gather Read Request & Response Visualization