## Slide 1: QuantSparse 3D Biweekly 2026-03-12
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch
Chi Zhang chizhang@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  Ventaglio – Integrated post-increment to Ventaglio, perf. benchmark
  3D System – Discussion on architecture and dataflow exploration
Timeline
Discussion

## Slide 3: Recap: Post-increment instruction extension
Ventaglio for high sparse ratio MatMul
  Objective: Eliminate explicit pointer updates  Improving VPU utilization when LMUL is small
  The post-increment semantics should be added to
    vle*.v: weight vectors
    fl*: scalar activations
    vlx*.v: index vectors
  Strip the post-increment semantics in Snitch  Forward bare load requests to Spatz
  In vanilla Spatz cluster:
    vle*.v: weight vectors
    fl*: scalar activations

## Slide 4: Post-increment instruction extension
Implementation finished
  Integrated post-increment extension with Ventaglio
    vle*.v: weight vectors
    fl*: scalar activations
    vlx*.v: index vectors
  Passed functional verification. Adapted the single-precision SpMM, SpMV kernels that uses the new instructions.
60.1%

## Slide 5: Post-increment instruction extension
Implementation status
  Integrated post-increment extension with Ventaglio
    vle*.v: weight vectors
    fl*: scalar activations
    vlx*.v: index vectors
  Passed functional verification. Adapted the single-precision SpMM, SpMV kernels that uses the new instructions.
    Removed explicit pointer updates
    VPU achieves maximum utilization in each inner-loop, no gap between MACC operations.
  Finished SpMM and SpMV HW-SW optimizations.
93.7%

## Slide 6: Other Improvements and Next Steps
Completed custom instruction extensions
  Added vfxmul.vf instruction, removed explicit Ventaglio memory unit reset;
  All custom instructions have LLVM and RISC-V opcodes supports.
New features and fixed bugs
  Simplified Ventaglio index-preload logic; removed complex preload FSM;
  Improved Ventaglio memory unit to vid mapping under loop-unrolling with simple shift logics;
  Fixed beat_counter in the scatter datapath for proper index refill.
New project launched
  SA – Integrating Ventaglio with VMXDOTP
    Inner-product dataflow; Bitmap indices for MX-blocks
Next step:
  Started Ventaglio modeling and calibration  End-to-end benchmark

## Slide 7: On 3D Architecture and Dataflow Exploration
Current status:
  In previous discussions, we examined the 3D mesh topology for stacking compute clusters in SoftHier.
  We also discussed the 3D systolic dataflow for GEMM operations.
Key questions need more discussion:
  Network Topology:
    Is a 3D mesh the optimal topology for this architecture?
    Should we explore alternative topologies with lower network diameter?
    What trade-offs arise in terms of latency, scalability, routing complexity, and physical layout?
  Architecture Organization :
    Is 3D stacking of compute tiles only the best architectural approach?
    What is the optimal compute-to-memory ratio for this architecture?
    How should memory and logic be organized to: Reduce thermal hotspots, Improve bandwidth and locality.
We Need a More Flexible and Extensible Architecture Description for 3D SoftHier !