## Slide 1: QuantSparse3D 2026-09-10 Bi-weekly
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch
Chi Zhang chizhang@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  Sparsity handling in memory endpoints, RTL and GVSoC model
Timeline
Discussion

## Slide 3: Recap: Sparse-capable DMA Extension
Idea
  Core configures the sparse transaction once
  DMA engine fetches the index stream and generate disaggregated AXI requests
  Additional semantics to cover:
    Address pointer to index stream in L1
    Per-index bit-width
    Index format (offset, bitmap…)

## Slide 4: Status: Sparse DMA Microarchitecture
Implementation status
  Frontend:
    New instruction added, decoder in frontend done;
    Verified sparse configurations captured by frontend;
  Midend:
    Standalone implementation finished
Integrated in Spatz DMA engine
  Passed functional verification
Gather kernel implementation with the new DMA instructions
  KV gather in Top-K sparse attention, with the same index stream
  Reached the same channel utilization (62.7%) as using AXI master

## Slide 5: Sparse DMA in GVSoC: Methodology
Goal
Reproduce RTL gather behavior in GVSoC
Target: within 10% cycle deviation
Approach
Same benchmark binaries and input data
Match the cluster and DRAM setup
One shared configuration for all cases
Same benchmark + input data
RTL reference
GVSoC model
Compare data + execution cycles
Refine shared timing

## Slide 6: Sparse DMA in GVSoC: Model Overview
Implementation
Sparse gather added to the GVSoC iDMA model
Indices select scattered source rows
DMA gathers rows into local memory
Matched test system
Spatz cores, local memory and DRAMSys
Runs the same three benchmark variants
Spatz cores
Configure
Sparse DMA
DRAMSys HBM
Read rows
Local memory (TCDM)
Indices
Gathered rows

## Slide 7: Sparse DMA in GVSoC: Test Coverage
Calibration matrix
3 variants × 4 workloads = 12 RTL / GVSoC comparisons
Gather sizes: 64, 128 and 256 rows
Sorted and shuffled index patterns
Functional checks
12 cases: indices, transfers and queuing
All data and completion checks pass
Four workloads × three variants
Workload
Core loop
Inlined loop
HW gather
128 rows / sorted
PASS
PASS
PASS
64 rows / sorted
PASS
PASS
PASS
256 rows / sorted
PASS
PASS
PASS
128 rows / shuffled
PASS
PASS
PASS
PASS = correct data + timing within 10%
Original DRAMSys example also passes

## Slide 8: Sparse DMA in GVSoC: Calibration Results
Target achieved
All 12 comparisons within 10%
Worst cycle deviation: 8.80%
Worst DMA-window deviation: 8.94%
Original hardware gather
1,236 RTL → 1,159 GVSoC cycles
-6.23% cycle deviation
Original gather experiment
RTL
GVSoC
0
1,000
2,000
3,000
3099
3056
Core loop
1952
1914
Inlined loop
1236
1159
HW gather
Software-measured cycles • 128 gathered rows
Accuracy validated on the measured gather workloads.

## Slide 9: Next Step: Sparse DMA
RTL model
  Backend implementation, area overhead analysis
GVSoC model
  Scale to multi-node system