## Slide 1: QuantSparse 3D Biweekly 2026-02-12
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  Ventaglio – Format extensions, loop-unrolled SpMM kernel, perf. benchmark
  3D System – 3D Systolic GEMM: dataflow and implementation
Timeline
Discussion

## Slide 3: Status Recap
Status:
  Ventaglio v0.4 RTL done; finished functional verification
  VPU utilization returns to ideal under small LMUL + loop unrolling (VLSU commit)
  Rerun the backend flow: negligible area overhead and no critical timing impact
Remaining tasks:
  [HW] More N:M formats  cost estimation
  [SW] SpMM kernel and collect performance benchmarks
  Design cleanup, back to GVSoC

## Slide 4: Extending Ventaglio Supported Format
Modular scatter/gather datapath in VTL
  Main goal: keep the design maintainable
  Approach: Refactored the datapath. New formats can be enabled by instantiating the additional datapaths with the proper N:M configuration.
  The control logic (e.g., index preloading and buffered indices) shared across all datapaths to avoid duplication.
  Results:
    Extended with 1:4 format. Passed functional verification.
    Adding one more format increases area by 12% (~6.9 kGE) @ VTL unit level  Matches expectations given the v0.4 area breakdown
      Memory unit: 41.6 kGE
      Datapath: 7.8 kGE
      Control: 5.7 kGE

## Slide 5: Loop-Unrolled SpMM Kernel
Implementation done and passed functional verification
  Currently supported settings:
    LMUL=4 @ 50% sparsity, LMUL=2 @ 25% sparsity (Constrained by the VTL Memory unit capacity)
  Waveform inspection shows ideal (100%) FPU utilization in the inner loop (2:4 format)
    Reason: With loop unrolling + Gustavson’s algorithm, the weight vector and its index vector are reused across multiple activation elements.

## Slide 6: Performance Analysis
Baseline implementation
  Scatter and gather using VSLDU
  Theoretical VPU utilization is 40%, measured utilization is 23% considering control overheads
  Unroll x2 SpMM kernel achieves ~2x AI comparing with SpMV
  Performance is constrained by VSLDU-to-VRF halved throughput with inefficient scatter/gather

## Slide 7: Performance Analysis
Scatter/Gather with Ventaglio
  Pushed the VPU utilization to the roofline
  With 2:4 format, N=64, P=64
    86.3% VPU utilization under SpMV workload
    93.1% VPU utilization under SpMM workload
  Memory-bound SpMV workload
    Cycles for loading indices cannot hide behind computaition
3.7x
4.1x
86.3%
93.1%

## Slide 8: Performance Analysis
Scatter/Gather with Ventaglio
  Pushed the VPU utilization to the roofline
  With 2:4 format, N=64, P=64
    86.3% VPU utilization under SpMV workload
    93.1% VPU utilization under SpMM workload
  Memory-bound SpMV workload
    Cycles for loading indices cannot hide behind computaition
  Utilization improves with larger N-dimension
    Mid-/Outer-loop control overhead becomes easier to amortize.
    Performance is comparable with the dense workload.
87.5%
97.9%

## Slide 9: Performance Analysis
Scatter/Gather with Ventaglio
  With 1:4 format, N=64, P=64
    SpMV remains at the roofline. Index loading overhead is comparably larger than 2:4 format
    SpMM performance drops
  Reason: VTL memory-unit capacity + Unrolling
    For dense GEMM, a common latency-hiding technique: more unrolling (e.g., 2× → 4×)
    For Ventaglio + Gustavson, this becomes expensive  must hold temporal accumulations in the VTL memory unit
    Unrolling along M-dimension requires multiple accumulation vectors resident simultaneously.
    With sparsity, the accumulation vector can expand relative to the weight vector  Lower LMUL supported
84.1%
60.1%

## Slide 10: Performance Analysis
Current supported settings (SEW=32, unroll=2×):
  LMUL=2 @ 1:4 sparsity format
  Memory unit capacity: 8192-bit, adding ~8% area @ Spatz core level.
  Cannot fully hide control overhead
Solutions:
  Increase memory-unit capacity, trading off area
  Introduce ‘post-increment’ semantics into RVV
84.1%
60.1%

## Slide 11: Ventaglio: Status and Next Step
Status:
  Ventaglio RTL wrap-up;
  Roofline model for performance analysis;
  Backend results analysis, area breakdown.
Remaining tasks:
  Design cleanup, back to GVSoC

## Slide 12: 3D Systolic GEMM on Cluster-Stacked System
Worked on 3D variant of systolic GEMM
Current assumptions:
  HBM still planar (attached on two base edges)
  Vertical links have same BW as planar ones
  For now: use RedMulE as compute (comparable to 2D SoftHier baseline)
In-layer flow remains the same
  Inputs (X) are streamed west to east, weights (W) south to north
  Output (Y) tiles are stationary, stored in south HBM once complete
  X, W are double-buffered in TCDM
HBM
HBM
HBM
HBM
HBM
HBM
HBM
HBM
HBM
HBM
HBM
HBM
HBM
X
HBM
HBM
HBM
HBM
z = 0 (base layer) view:
Like 2D systolic GEMM, but narrower W, Y tiles: distributed among stacked clusters. Output Y is stationary.
W

## Slide 13: 3D Systolic GEMM: Vertical Dataflow
Partition W tiles among layers
  South-edge clusters “pull up” tiles fetched from HBM in base layer
  Only used subtiles are moved / kept
  Local subtile is streamed north
Full X tiles reused among layers
  West edge “pulls up” full X tiles  reuse
  Tiles then streamed west as in 2D
Finished Y tiles written back directly
  As in 2D, clusters close to HBM start and finish first  low contention
HBM
w0
w1
w2
w3
w1
w2
w3
w2
w3
w3
z
y
HBM
z
y
x
x
x
x

## Slide 14: 3D Systolic GEMM: Status and Next Steps
Current status:
  Implemented first version of 3D kernel
  Debugging implementation in GVSoC
Next steps:
  Measure performance benefits of 3D stacking vs. 2D SoftHier
  Analyze layer scaling and optimize implementation
  Implement further kernels (e.g. Attention)