## Slide 1: QuantSparse 3D Biweekly 2026-02-26
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Chi Zhang chizhang@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  Ventaglio – Post-increment semantics for RVV, perf. benchmark
  3D System – First systolic 3D GEMM evaluation and analysis
Timeline
Discussion

## Slide 3: Recap: Performance Analysis
Ventaglio status:
  Ventaglio RTL wrap-up;
  Roofline model for performance analysis;
  Backend results analysis, area breakdown.
Current supported settings (SEW=32, unroll=2×):
  LMUL=2 @ 1:4 sparsity format
  Memory unit capacity: 8192-bit, adding ~8% area @ Spatz core level.
  Cannot fully hide control overhead
Solution:
  Introduce ‘post-increment’ semantics into RVV
84.1%
60.1%

## Slide 4: Post-increment instruction extension
Ventaglio for high sparse ratio MatMul
  Objective: Eliminate explicit pointer updates  Improving VPU utilization when LMUL is small
  The post-increment semantics should be added to
    vle*.v: weight vectors
    fl*: scalar activations
    vlx*.v: index vectors
  Two possible implementation approaches:
    Option 1: Handle decoding in the Spatz controller  Need to add logics in both Snitch and Spatz decoder
    Option 2: Strip the post-increment semantics in Snitch  Forward bare load requests to Spatz

## Slide 5: Post-increment instruction extension
Implementation status
  Starting from the vanilla Spatz cluster, implemented the new instructions
    vle*.v: weight vectors
    fl*: scalar activations
  Passed functional verification. Adapted the single-precision MatMul kernel that uses the new instructions.
    Able to remove all pointer-update instructions.  The number of instructions in the inner loop is reduced by ~50%. (Consider loop unrolling.)

## Slide 6: Post-increment instruction extension
64x64x64 GEMM workload with LMUL=2
  With constrained LMUL settings, baseline VPU utilization is hindered by the overhead of control instructions.
  Post-increment extension improves VPU utilization
  With the VLSU commit logic optimization, the utilization is expected to be `at-the-roofline`.
Next step:
  Merge the change with Ventaglio, benchmark
  Work with Chi on Ventaglio modeling and calibration
75.7%
45.9%
90.5%
74.4%
1.6x
1.2x
97.4%
98.1%

## Slide 7: 3D Systolic GEMM on Cluster-Stacked System
First measurements on systolic GEMM
  Improved weight dataflow
What remains the same
  Same in-layer dataflow: X east-west, W south-north, Y stored south
  Same X tile, different W tiles per layer
What changed: W tile distribution
  Before: partition W tiles, pass along sub-tiles
  Now: each layer gets its own full W tile directly from HBM (no systolic Z movement)
  No risk of underutilizing RedMulE
  Better TCDM utilization & arith. intensity
HBM
HBM
HBM
HBM
HBM
HBM
HBM
HBM
HBM
W
X
z
y
HBM
z
y
HBM
w0
w1
w2
w3

## Slide 8: 3D Systolic GEMM: Performance Results
Chart: 
| 4x4x1 | 4x4x2 | 4x4x4
3D Speedup | 1 | 1.7849 | 2.9833
Ideal 3D Speedup | 1 | 2 | 4
Chart: 
| 4x4x1 | 4x4x2 | 4x4x4
3D Speedup | 1 | 1.7849 | 2.9833
Ideal 3D Speedup | 1 | 2 | 4
Local link util at (0,0,0) | 0.4322 | 0.5995 | 0.8576
Good scaling for stacked layers
  2 layers: 1.78× faster
  4 layers: 2.98× faster
Scaling losses due to
  Increased systolic delay
  Longer writeback phase
  At ≥4 layers: local link bottleneck
Limitation: local link at origin must move twice the HBM data
  Must copy in weights (S) and inputs (W)
  Limits sum of S and W HBM utils to 100%
  Local link util saturates at 4 layers (86%)
Speedup
Local link utilization

## Slide 9: 3D Systolic GEMM: Status and Next Steps
Current status:
  3D Systolic kernel running, demonstrating speedups until bound by local link
Next steps:
  Investigate dataflows that avoid local link bottleneck (perhaps input/weight stationary)
  Implement parametric 3D links (BW, arity)
  Implement further kernels (e.g. Attention)