## Slide 1: QuantSparse 3D Biweekly 2026-04-16
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch
Chi Zhang chizhang@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  Ventaglio – E2E framework adaptation, benchmark, and paper status
  3D System – FlooNoC model in GVSoC
Timeline
Discussion

## Slide 3: Recap: Ventaglio E2E Simulation on SoftHier
Work in progress
  Spatz SUMMA optimizer: L1 capacity constraint for double-buffered tiling and dataflow
  Adaptation to GEMV/SpMV for autoregressive decoding
Next step
  E2E pipeline integration: Add Spatz-base SUMMA implementations to the flow pipeline
  3-way comparison (dense, 2:4 sparse, and 1:4 sparse) on Qwen-7B

## Slide 4: Ventaglio E2E Simulation on SoftHier
E2E flow integration finished
  GVSoC modeling of the new Ventaglio instruction extensions
  Multi-cluster Spatz sparse tensor contraction kernel using SUMMA dataflow
    Drop-in replacement for the RedMule-based implementation
  Sparse-aware SUMMA DMA
    Loading weight with aware of sparsity formats  both DMA and compute scale with sparsity
Dense model runtime breakdown and analysis
  Model: Qwen-7B (embed=4096, 32 heads GQA, MLP=22016)
  At seq=2048, attention grows ~2% runtime in both prefill and autoregressive decoding phases
    Linear projection dominates runtime

## Slide 5: Ventaglio E2E Simulation on SoftHier
Performance analysis
  Model level (measured under Qwen-7B, seq=2048)
    Prefill: 1.91x and 3.53x speedup
    Autoregressive decode: 1.85x and 3.41x speedup with 2:4 and 1:4 format, respectively  due to fixed attention and data movement overhead
Next step: add activation sparsity to the flow
  ActSparse-GEMM kernel implemented and integrated to the E2E flow
  Benchmark on LlaMA-3-8B, with Duo-GPT pruned 50% activation sparsity + 50% weight sparsity

## Slide 6: Updating FlooNoC Model in GVSoC
In original FlooNoC model (both 2D and 3D mesh):
  Hard-coded Router-to-Router link with fixed latency.
  Homogeneous connections: every link has the same bandwidth.
We are refactoring the FlooNoC GVSoC model:
  For model close to reality:
  Eg, 3D Mesh’s Z direction links may have different latency and bandwidth than links on XY directions
  We need to give these flexibilities on NoC modeling
  We have a master student project working on this topic currently
  Will futher discuss dataflow for applications once the new FlooNoC model is stable