## Slide 1: SoftHier Project Closure Report – PULP Team Side
Chi Zhang chizhang@iis.ee.ethz.ch
Luca Colagrande colluca@iis.ee.ethz.ch
Thomas Benz tbenz@iis.ee.ethz.ch

## Slide 2
Introduction to SoftHier Project
End of Dennard Scaling
  Leads to "power wall" across computing systems, from mobile to supercomputers.
  Hardware-software codesign critical to improving performance under tight power constraints.
Shift to Massively Parallel Architectures
  Scaling to thousands of Processing Elements (PEs) essential for power-efficient performance.
  Embarrassingly parallel workloads (e.g., Large Language Models) driving the need for KiloPE architectures.

## Slide 3
Introduction to SoftHier Project
Core Challenges in Memory Hierarchy
  Instruction Memory Bottlenecks
    Demand for domain-specific ISAs to efficiently manage thousands of operations with single instructions.
    Amortizing instruction fetches reduces energy impact on the instruction memory.
  Data Memory Bottlenecks (The "Memory Wall")
    High-bandwidth demands from PEs challenge traditional memory architectures.
    Scaling KiloPEs requires novel solutions beyond classical cache hierarchies.
GH200
FP16 FlashAttn on GH200
FP16 GEMM on GH200
Perf Gap
64%
36%
Gap
55%
28%

## Slide 4
SoftHier Project Objective
This goal will be achieved thanks to
  An increased level of automation in the programming tool flow
  The use of domain-specific languages and abstractions.
  Hardware enhancements in the memory hierarchy that facilitate automatic instantiation of accelerated data-motion primitives from abstract, streamlined software APIs.
Work Package for PULP team
  Aims at architecture exploration, sizing and design of advanced functions related to data motion subsystems (SPM, DMA, NoC, memory controllers) to assess their hardware cost and to analyze the efficiency of the new architecture on the targeted applications
The objective of SoftHier is to drastically reduce hardware inefficiency by replacing caches with software-managed, efficient SPMs and DMAs, while maintaining programming effort low for the application developer
Prof. Torsten Hoefler’s Group
Our PULP Group

## Slide 5
Template Architecture Overview Tile-Based Many-PE
Tile-based many-PE accelerators
  Structured as meshes of compute tiles
    Matrix, vector and scalar engines
    Local explicitly managed memories
  Interconnect with scalable NoC topology
  Main memory positioned at die boundaries
Favors silicon efficiency and scalability
  A dense compute tile placement
  Software-controlled partitioned memory hierarchy
  Eliminates L2 on-chip cache for area efficiency
Examples
  Tesla’s Dojo, Tenstorrent’s Blackhole
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
HBM CTRL
CH0
CH1
…
CHn
HBM CTRL
CH0
CH1
…
CHn
HBM CTRL
CH0
CH1
…
CHn
HBM CTRL
CH0
CH1
…
CHn
I$
Matrix engine
L1 local memory
DMA
Scalar core
Vector engine
interconnect
To Router
SM
HBM CTRL
HBM CTRL
HBM CTRL
L2 Cache
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
L1
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
HBM CTRL
HBM CTRL
HBM CTRL
Tile-Based Many-PE
vs Nvidia GPU Arch

## Slide 6
High-Level Simulation Model – SoftHier System
Fully Parameterizable through Configuration File
  System configuration
    #Tiles (#row, #column)
    NoC link data width
    #HBM channels and placement on 4 edges
  Cluster configuration
    L1 memory capacity and bandwidth
    Matrix engine systolic array (shape, CE pipeline stage)
    DMA burst length, #outstanding burst
Based on GVSoC[1] Platform
  Event-based simulator, fast simulation speed up to 25 MIPS
Calibrated with RTL Models
https://github.com/gvsoc/gvsoc/tree/soft_hier_release
Core 0
Core 0
…
Core n
Matrix
Engine
DMA
I $
L1 local memory
Vector
Engine
Interconnect
To DATA NoC Router
To SYNC NoC Router
TE Cluster
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
HBM
HBM
HBM
HBM
R
R
Data NoC Router
Sync NoC Router

## Slide 7
Review of Work Package – PULP Team Side
Define Baseline Template Architecture (M1-WP1)
Develop a High-Level Simulation Model (M1-WP1)
PPA Estimation (M2-WP1)
Specification and Preliminary Modelling and Analysis of Optimized Architecture (M3-WP1)
  Based on the insight gathered in the first year of work, the memory hierarchy components will be tuned and optimized to facilitate programming and boost performance. The proposed hardware enhancements will be prototyped and their cost performance benefits will be assessed with microkernels.
Performance and Energy Estimation and Benchmarking (M4-WP1-WP2)
  Benchmarking report on hardware-software integration between the two WPs, demonstrating targeted transformations to optimize and streamline performance for CLOUDSC cloud microphysics scheme and the LULESH hydrodynamics solver as well as ML applications. Detailed performance study with different application configurations and comparing various workflow options. For Ascend, we will aim at mapping deep-Learning kernels such as Transformer Decoders. (Report & Open-source release)
2nd Year
1st Year

## Slide 8
Review of Work Package – PULP Team Side
For the 2nd Year, We have done
  Proposed Architectural Optimization (M3-WP1):
    Lightweight high-throughput collective capable NoC
    RTL prototyping
  Dataflow and NoC collective primitives co-design for key LLM kernels (M4-WP1-WP2)
    FlatAttention for MHA and variants for GQA, MQA, DeepSeek MLA
  End-to-End Performance Analysis for DeepSeekV3 Inference (M4-WP1-WP2)

## Slide 9
M3-WP1: Lightweight High-Throughput Collective Capable NoC
RTL Extension on NoC
  Multicast + Reduction support on NoC router
  Use FPUs inside tile for reduction operations
Model in GVSoC for SoftHier
  Calibration with RTL, Average Runtime cycle deviation is around 16%
RTL Area analysis
  Multicast adds 5.8% area overhead on router
  Full Multicast + Reduction adds 16.9% area
Chart: Transfer Size (KiB)
| 2 | 3 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
RTL | 86 | 107 | 125 | 189 | 261 | 331 | 403 | 467 | 539 | 613
GVSoC | 61 | 79 | 97 | 161 | 225 | 289 | 353 | 417 | 481 | 545
Deviation(%) | 0.2907 | 0.26168 | 0.224 | 0.14815 | 0.13793 | 0.12689 | 0.12407 | 0.10707 | 0.10761 | 0.11093
Calibration
Area Overhead
NoC Extension in RTL

## Slide 10
LLM workloads have become increasingly impactful
  DeepSeek-V3, ChatGPT, Llama
Dominating LLM are Transformer-based
The attention bottleneck
  Multi-Head Attention (MHA) exhibits quadratic complexity over sequence length. O(S2)
  Most operations in MHA are bottlenecked by memory accesses[2]
  Performance bottleneck for
    LLM training
    LLM inference
      long context prefill and decode
Q
Attention Score
KT
D
S
S
O
SoftMax(Att.Score)
S
V
(1).
(2).
(3).
Multi Heads
M4-WP1-WP2: The Attention Bottleneck in Transformer LLMs

## Slide 11
M4-WP1-WP2: The Attention Bottleneck in Transformer LLMs
With LLM model architecture evolution, Attention is becoming dominated
  MHA + MLP in llama, qwen  MLA + MoE in DeepSeek, Kimi-v2
  Attention kernels are not performing good enough on commercial GPUs in both prefill and decode stage
    Optimized implementation for GPU: FlashAttention[3] by Tri Dao, FlashMLA[4] by DeepSeek team
Prefill FlashAttn on GH200
Decode FlashMLA on GH200
Model FLOP Breakdown - Prefill
Model FLOP Breakdown - Decode
MHA + MLP
MLA + MoE
MLA + MoE
MHA + MLP
MLA + MoE
MLA + MoE
Gap
Gap

## Slide 12
We are targeting attention kernels on tile-based many-PE architecture. The goal is:
  Achieve high utilization of the tiles’ matrix engines
  Minimize energy-hungry off-chip accesses
Architecture and dataflow need to be co-explored
  Dataflow leverages HW feature, e.g., collective primitives on NoC fabric
M4-WP1-WP2: Dataflow and NoC Collective Primitives Co-Design

## Slide 13
We are targeting attention kernels on tile-based many-PE architecture. The goal is:
  Achieve high utilization of the tiles’ matrix engines
  Minimize energy-hungry off-chip accesses
Architecture and dataflow need to be co-explored
  Dataflow leverages HW feature, e.g., collective primitives on NoC fabric
    Accelerate inter-tile collective communications
  Demonstrate attention workloads can be mapped more efficiently on tile-based architectures by leveraging collective communications on NoC
M4-WP1-WP2: Dataflow and NoC Collective Primitives Co-Design

## Slide 14
M4-WP1-WP2: FlatAttention Motivation
Analysis start from FlashAttention
  Fuse microkernels of each head attention
  MHA workload is partitioned to tiles over:
    Batch size, number of heads, output sequence dimension
  Every tile processes independently
    Every tile need to access in HBM
    No communication between tiles is required
  Results in an HBM I/O complexity of
    Sequence length S, head dimension D, number of heads H, batch size B and block size M:=Br=Bc
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Q: S x d
KT: d x S
V: S x d
d x Bc
Br x d
Bc x d
Copy Block to SRAM
Copy
Copy
Inner Loop
Inner Loop
Outer Loop
Outer Loop
Output to HBM
sm(QKT)V: S x d
Br x Bc

## Slide 15
FlatAttention – Redefine how MHA is parallelized
  Leverages multiple tiles as a unified entity
  Process an MHA block of a significantly larger size
    The aggregate L1 memory of a group of tiles
    Collectively store the block
  When N tiles are grouped together, HBM I/O complexity:
  More tiles are grouped, less HBM accesses needed
Q: S x d
KT: d x S
V: S x d
d x Bc
Br x d
Br x Bc
Bc x d
Copy Block to SRAM
Copy
Copy
Inner Loop
Inner Loop
Outer Loop
Outer Loop
Output to HBM
sm(QKT)V: S x d
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
M4-WP1-WP2: FlatAttention Motivation

## Slide 16
HBM for KT & V
HBM for O & Q
M4-WP1-WP2: Detailed FlatAttention Dataflow
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
KT
O
Q
Attention Score
Gy
V
Bc
Bc/Gx
Gx
Bc
Bc/Gx
Br
Br/Gy
Distinct data movement patterns within the tile group
  Edge tiles collect data from HBM once and inter-tile data exchange via collective communications
O
Att
KT
Q
m l e l-1 m-1
O
Att
KT
Q
m l e l-1 m-1
O
Att
KT
Q
m l e l-1 m-1
O
Att
KT
Q
m l e l-1 m-1
Load Q and row-wise multicast
V
V
V
V
1
O
Att
KT
Q
m l e l-1 m-1
O
Att
KT
Q
m l e l-1 m-1
O
Att
KT
Q
O
Att
KT
Q
m l e l-1 m-1
m l e l-1 m-1
Load KT V and col-wise multicast
V
V
V
V
2
O
S
KT
Q
m l e l-1 m-1
O
S
KT
Q
m l e l-1 m-1
O
S
KT
Q
O
S
KT
Q
m l e l-1 m-1
m l e l-1 m-1
Calculate att.score, scaling, and local rowmax m
V
V
V
V
3
m l e l-1 m-1
m l e l-1 m-1
Row-wise red.max m and multicast
O
S
KT
Q
m l e l-1 m-1
O
S
KT
Q
m l e l-1 m-1
O
S
KT
Q
O
S
KT
Q
m l e l-1 m-1
m l e l-1 m-1
V
V
V
V
4
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
O
P
KT
Q
m l e l-1 m-1
m l e l-1 m-1
Calculate softmax numerator P and demoninator l
V
V
V
V
5
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
O
P
KT
Q
m l e l-1 m-1
m l e l-1 m-1
Row-wise red.sum l and multicast
V
V
V
V
6
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
O
P
KT
Q
m l e l-1 m-1
m l e l-1 m-1
Calculate and update local O & tracking statistics l-1 , m-1
V
V
V
V
7
m l e l-1 m-1
m l e l-1 m-1
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
O
P
KT
Q
Finalize O with demoninator , row-wise red.sum and store back to HBM
m l e l-1 m-1
m l e l-1 m-1
V
V
V
V
8
Tiling Scheme

## Slide 17
M4-WP1-WP2: Asynchronous FlatAttention
To further improve utilization
  Using asynchronization nature of {DMA, Matrix, Vector} engines invoking
  One tile group dealing with 2 heads concurrently
  Overlap the runtime of {DMA, Matrix, Vector} engines
O
Att
KT
Q
m l e l-1 m-1
Naïve FlatAttention
x1
V
DMA
Matrix
Engine
Vector
Engine
O
Att
KT
Q
m l e l-1 m-1
x2
V
Asynchronous FlatAttention
DMA
Matrix
Engine
Vector
Engine

## Slide 18
M4-WP1-WP2: FlashAttention vs. FlatAttention
Compare different MHA implementations
  FlashAttention-2(FA-2) and FlashAttention-3 (FA-3)
  Naïve FlatAttention without (Flat) and with (FlatColl) Collective primitves on NoC fabric.
  Asynchronous FlatAttention (FlatAsyn) with NoC collective primitives
With FlatAttention group includes all tiles
Results
  FlashAttention is highly memory-bound
  FlatAttention significantly reduces HBM access
  NoC supported collective primitives are essential to accelerate inter-tile data exchange
  With NoC collective primitives + Asynchronous:
    Up to 89.3% uti, 4.1× perf speedup, 16× less HBM traffic

## Slide 19
M4-WP1-WP2: FlashAttention on GH200 vs. FlatAttention on SoftHier
Configure SoftHier with the same {FLOPS@FP16, HBM BW} to GH200
  Estimate die area cost from reference RTLs
  1.8x die size reduction to GH200 (TSMC 5nm)
Generalize FlatAttention to variants like GQA & MLA
  C: compute-bound and uti; M: memory-bound and BW uti
  Avg {C: 86%,M:78%}, Avg 1.9x speedup to solution on GH200
Prefill MHA
Decode MHA
Decode GQA
Decode MLA

## Slide 20
M4-WP1-WP2: Full DeepSeek-671B Decoding on SoftHier
Workload
  Full DeepSeekv3-671B
  FP8 Decoding with Multi Token Prediction (MTP) enabled
Chip Spec
  Configure SoftHier with the same {FLOPS@FP8, HBM BW} to GH200
System Spec
  64-Chip system to store 671B parameters
  Chip2Chip Interconnect in a 2D Mesh topology
  Chip2Chip Link
    256ns latency
    1TB/s bandwidth
Chip
HBM4
HBM4
C2C Router
C2C Link
Lat = 256ns
BW = 1TB/s

## Slide 21
M4-WP1-WP2: Full DeepSeek-671B Decoding Parallelism Scheme
SoftHier
Chip 0
SoftHier
Chip 1
SoftHier
Chip 2
SoftHier
Chip 63
……
C2C Interconnect
Expert 0
Expert 1
Expert 2
Expert 3
Expert 4
Expert 5
Expert 6
Expert 7
Expert 8
Expert 9
Expert 10
Expert 11
Expert 252
Expert 253
Expert 254
Expert 255
SoftHier
Chip 0
SoftHier
Chip 1
SoftHier
Chip 2
SoftHier
Chip 63
……
k
k
k
k
User/Chip
k
k
k
k
k
k
k
k
k
k
k
k
SoftHier
Chip 0
SoftHier
Chip 1
SoftHier
Chip 2
SoftHier
Chip 63
……
SoftHier
Chip 0
SoftHier
Chip 1
SoftHier
Chip 2
SoftHier
Chip 63
……
MLA + Shared Expert + Gate
Dispatch
Combine
Routed Expert
Time
User/Chip
User/Chip
User/Chip
SoftHier
Chip 0
SoftHier
Chip 1
SoftHier
Chip 2
Layer 0
Layer 1
Layer 2
k
k
k
k
SoftHier
Chip n
Layer n
User/Chip
Pipeline Parallelism (PP)
  Each Chip decode for one layer
  C2C communicate only inter-layer tokens
Full Expert Parallelism (EP64)
  Each chip decode for all layers, except for MoE routed experts
  Routed experts are distributed over all chips
  C2C communication deals with token dispatch to experts and combine results of experts
Hybrid Parallelism
  Eg: EP16-PP4
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
EP
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
EP
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
EP
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
EP
PP
PP
PP

## Slide 22
M4-WP1-WP2: Flat vs Flash for DeepSeek-671B Decoding
Benchmark E2E decoding performance on SoftHier Chip Systems @EP32-PP2
  Varying users per chip (b), plot the throughput of 64-Chip system vs. time per output token (TPOT) each user
    Compare: MLA implemented with proposed FlatAttention (FlatMLA) dataflow v.s using FlashMLA dataflow
    @user/chip=256: FlatMLA speedup MLA 4.5x on SoftHier, resulting an E2E speedup of 2.1x
    If compared to FlashMLA on GH200 : FlatMLA on SoftHier has 2.2x speedup, and E2E speedup of 1.4x (assuming other kernels runtime are the same)
FlatMLA
FlashMLA
4.5x
E2E Decode Speedup 2.1x
Better

## Slide 23
M4-WP1-WP2: Expert Parallelism Trade-off
Effects of Expert Parallelism Scale
  Target time per output token (TPOT) for each user: <50ms
  Lager EP  Optimize TPOT and Throughput
  Lager EP  C2C Communication overhead increase  Decrease throughput at TPOT constraint
Better

## Slide 24
M4-WP1-WP2: SoA Comparison
Better
Comparing to SoA DeepSeek Decoding
  SoftHier System uses the EP32-PP2 configuration
    Varies the C2C link bandwidth
  Normalized to throughput per chip
  Compare to SoA: Under 50ms TPOT constraint:
    SoftHier C2C link BW = 1TB/s
      2.9x speedup to DeepSeek profile[3] on H800
      3.6x speedup to CloudMatrix-Infer[4]
    SoftHier C2C link BW = 200GB/s
      1.6x speedup to DeepSeek profile on H800
      1.9x speedup to CloudMatrix-Infer
DeepSeek Profile on H800
CloudMatrix-Infer
Best TPOT
CloudMatrix-Infer
Best Throughput
System | Number of Chips | Chip Interconnect Method | HBM BW per Chip | HBM capacity per Chip | TFLOPS per Chip | User/Chip | KV Cache Length | Throughput per Chip (token/s/chip) | TPOT (ms)
CloudMatrix-Infer on Acsend 910C | 384 | Multi-Plane (UB: 382 GB/s, RDMA: 400 Gbps, VP: 400 Gbps per Chip) | 3.2 TB/s | 128GB | 1504@INT8 | 128 | 4096 | 1943 | 49.4
DeepSeek Profile on H800 | 96 | Multi-Plane (NVLink: 160 GB/s, RDMA: 400 Gbps per Chip) | 3.6 TB/s | 80GB | 1979@FP8 | 128 | 4096 | 2325 | 50.2
SoftHier System Solution | 64 | 8x8 2DMesh: 1TB/s per Chip | 4.0 TB/s | 128GB | 1979@FP8 | 256 | 4096 | 6940 | 35.8
SoftHier System Solution | 64 | 8x8 2DMesh: 200 GB/s per Chip | 4.0 TB/s | 128GB | 1979@FP8 | 128 | 4096 | 3773 | 33.1

## Slide 25
SoftHier Project Conclusion – PULP Team Side
For better HW efficiency we proposed
  Lightweight high-throughput collective capable NoC
  Dataflow and NoC collective primitives co-design for key LLM kernels
We achieved
  Area Efficiency: 1.8x die size reduction to GH200 @same {FLOP, HBM BW}
  Energy Efficiency: 16× HBM traffic reduction on the key Attention Kernel
  Performance: up to 3.2x speedup in attention kernel vs. solution on GH200, and 2.9x speedup in DeepSeekv3 decoding over SoA solution.
The objective of SoftHier is to drastically reduce hardware inefficiency by replacing caches with software-managed, efficient SPMs and DMAs, while maintaining programming effort low for the application developer
Published: ISVLSI 2025
Submitted: MLSys 2026
Submitted: DAC 2026
To submit

## Slide 27
References
[1] N. Bruschi et al., “GVSoC: a highly configurable, fast and accurate full-platform simulator for RISC-V based IoT processors,” in ICCD, 2021.
[2] A. Ivanov et al., “Data movement is all you need: A case study on optimizing transformers,” in MLSys, 2021.
[3] J. Shah et al., “FlashAttention-3: Fast and accurate attention with asynchrony and low-precision,” in NeurIPS, 2024.
[4] Chenggang Zhao et al. “DeepGEMM: clean and efficient FP8 GEMM kernels with fine-grained scaling”. https://github.com/deepseek-ai/DeepGEMM, 2025.
[5] DeepSeek-AI. 2025. Profiling Data in DeepSeek Infra. https://github.com/deepseek-ai/profile-data. Accessed: 2025-05-21.
[6] Zuo, Pengfei, et al. "Serving Large Language Models on Huawei CloudMatrix384." arXiv preprint arXiv:2506.12708. 2025.