## Slide 1: SoftHier First-Year Stage Report
Chi Zhang chizhang@iis.ee.ethz.ch
Thomas Benz tbenz@iis.ee.ethz.ch
Luca Colagrande colluca@iis.ee.ethz.ch

## Slide 2
Motivation of SoftHier Project
End of Dennard Scaling
  Leads to "power wall" across computing systems, from mobile to supercomputers.
  Hardware-software codesign critical to improving performance under tight power constraints.
Shift to Massively Parallel Architectures
  Scaling to thousands of Processing Elements (PEs) essential for power-efficient performance.
  Embarrassingly parallel workloads (e.g., ML, large-scale simulations) driving the need for KiloPE architectures.
Core Challenges in Memory Hierarchy
  Instruction Memory Bottlenecks
    Demand for domain-specific ISAs (e.g., vector, tensor operations) to efficiently manage thousands of operations with single instructions.
    Amortizing instruction fetches reduces energy impact on the instruction memory.
  Data Memory Bottlenecks (The "Memory Wall")
    High-bandwidth demands from PEs challenge traditional memory architectures.
    Scaling KiloPEs requires novel solutions beyond classical cache hierarchies.

## Slide 3
SoftHier Project Objective
This goal will be achieved thanks to
  An increased level of automation in the programming tool flow
  The use of domain-specific languages and abstractions.
  Hardware enhancements in the memory hierarchy that facilitate automatic instantiation of accelerated data-motion primitives from abstract, streamlined software APIs.
Work Package for PULP team (WP1)
  Aims at architecture exploration, sizing and design of advanced functions related to data motion subsystems (SPM, DMA, NoC, memory controllers) to assess their hardware cost and to analyze the efficiency of the new architecture on the targeted applications
The objective of SoftHier is to drastically reduce hardware inefficiency by replacing caches with software-managed, efficient SPMs and DMAs, while maintaining programming effort low for the application developer

## Slide 4
Review of First-Year Work Package
Define Baseline Template Architecture (M1-WP1)
  Featuring KiloPE Tensor Engines (TEs) with explicitly managed L1 memory buffers through tightly coupled DMA engines
  The TEs will be based on the RISC-V ISA, enhanced with tensor instructions to directly manage the large tensor units
  TEs will be connected through a NoC, which will also provide access to L2 memories and main memory
Develop a High-Level Simulation Model (M1-WP1)
  Enable high-level performance estimation and early software development
  Based on the Banshee[1] binary translation simulator
  Establish the modeling environment, the main architectural parameters, and develop the hardware models for all components
  Set up the basic hardware abstraction layers and APIs to support the software layers developed in WP2
PPA estimation (M2-WP1)
  Hardware will also be designed in parametric RTL to enable power, performance, and area (PPA) assessment in multiple instantiations.
[1] Riedel, Samuel, et al. "Banshee: A fast LLVM-based RISC-V binary translator." 2021 IEEE/ACM International Conference On Computer Aided Design (ICCAD). IEEE, 2021.

## Slide 5
Review of First-Year Work Package -- Changes
Define Baseline Template Architecture (M1-WP1)
  Featuring KiloPE Tensor Engines (TEs) with explicitly managed L1 memory buffers through tightly coupled DMA engines
  The TEs will be based on the RISC-V ISA, enhanced with tensor instructions to directly manage the large tensor units
  TEs will be connected through a NoC, which will also provide access to L2 memories and main memory
Develop a High-Level Simulation Model (M1-WP1)
  Enable high-level performance estimation and early software development
  Based on the Banshee[1] binary translation simulator
  Based on the GVSoC[2] fast and accurate full-platform simulator
  Establish the modeling environment, the main architectural parameters, and develop the hardware models for all components
  Set up the basic hardware abstraction layers and APIs to support the software layers developed in WP2
PPA Estimation (M2-WP1)
  Hardware will also be designed in parametric RTL to enable PPA assessment in multiple instantiations.
[1] Riedel, Samuel, et al. "Banshee: A fast LLVM-based RISC-V binary translator." 2021 IEEE/ACM International Conference On Computer Aided Design (ICCAD). IEEE, 2021.
[2] Bruschi, Nazareno, et al. "GVSoC: a highly configurable, fast and accurate full-platform simulator for RISC-V based IoT processors." 2021 IEEE 39th International Conference on Computer Design (ICCD). IEEE, 2021.

## Slide 6
M1-WP1: Baseline Template Architecture – RedMule Engine
RedMule[3] – The Tensor Engine
  Developed by PULP team with open-sourced RTL
  Reduced-precision matrix multiplication engine
  Supporting mixed-precision floating point (FP16/FP8) arithmetic
  Accelerates general matrix-matrix operations (GEMM-Ops)[4]
  2-Dimensional array of CEs (Compute Elements)
  Systolic-like structure
RISC-V ISA extensions
  mcnfig – Set GEMM M, N, K parameters
  marith – Set X,W,Y matrix address + start RedMule
mcnfig Instruction
marith Instruction
[31:16] [15:0]
K size M size
[31:0]
N size
[31:0]
Y addr
[31:0]
W addr
[31:0]
X addr
[3] Tortorella, Yvan, et al. "RedMule: A mixed-precision matrix–matrix operation engine for flexible and energy-efficient on-chip linear algebra and TinyML training acceleration." Future Generation Computer Systems 149 (2023): 122-135.
[4] Zhang, Yunan, Po-An Tsai, and Hung-Wei Tseng. "SIMD2: A generalized matrix instruction set for accelerating tensor computation beyond GEMM." Proceedings of the 49th Annual International Symposium on Computer Architecture. 2022.

## Slide 7
TCDM (Multi-banked L1)
M1-WP1: Baseline Template Architecture – TE Cluster
Snitch – Tiny RISC-V Core
  Single-stage, small integer control core
Instruction Cache
  Shared among all cores
CTRL Registers
  Used for synchronization within the cluster
  Store useful information (e.g. Cluster ID)
TCDM – Multi-banked L1
  Explicitly managed L1 memory
iDMA
  Move data in/out of L1
RedMule – The Tensor Engine
Snitch
Core 0
Snitch
Core N
RedMule
iDMA
CTRL
REG
…
I $
Wide Bus
TCDM Interco
HWPE Interco
DMA to
TCDM
Bank
0
Bank
1
Bank
2
Bank
M
…
TE Cluster

## Slide 8
M1-WP1: Baseline Template Architecture – System
Core 0
Core 0
…
Core n
RedMule
iDMA
I $
TCDM (Multi-banked L1)
CTRL
REG
Interconnect
To Data NoC Router
To Sync NoC Router
TE Cluster
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
HBM
HBM
HBM
HBM
R
R
Data NoC Router
Sync NoC Router
System Level
  TE Clusters in 2D-Mesh, HBM as main memory
  TE Clusters and HBM CTRL are connected by NoC
  NoC enables
    Cluster L1<->HBM, Cluster L1<->Cluster L1
  Data NoC -- wide link, iDMA transfer bulk data
  Sync NoC – narrow link, Snitch core remote access for global synchronization purpose

## Slide 9
M1-WP1: High-Level Simulation Model – GVSoC Simulator
Change Plan: Banshee -> GVSoC
  Banshee[1] : Binary Translation Simulator
  GVSoC[2] : Fast and Accurate Full-Platform Simulator
Reasons
  Banshee is only a functional simulator for RISCV binaries, no timing model and cannot accurately evaluate performance
  GVSoC is an event-based simulator, providing accurate timing (< 10% runtime deviation vs. FPGA emulation of PULP IPs)
  GVSoC is fast, achieving a simulation speed of 25 MIPS (measured with a 16-core PULP cluster)
GVSoC
Banshee
[1] Riedel, Samuel, et al. "Banshee: A fast LLVM-based RISC-V binary translator." 2021 IEEE/ACM International Conference On Computer Aided Design (ICCAD). IEEE, 2021.
[2] Bruschi, Nazareno, et al. "GVSoC: a highly configurable, fast and accurate full-platform simulator for RISC-V based IoT processors." 2021 IEEE 39th International Conference on Computer Design (ICCD). IEEE, 2021.

## Slide 10
M1-WP1: High-Level Simulation Model – Integrate DRAMSys
DRAMSys5.0 (© Fraunhofer IESE):
  A flexible DRAM subsystem simulator
  Based on SystemC TLM-2.0, event-driven, fast simulation, JEDEC standard
  Support accurate simulation of DDR4, DDR3, HBM2, HBM2E, LPDDR4
Integration with GVSoC
  Synchronization of DRAMSys (SystemC) and GVSoC time engine
  Interface bridge between DRAMsys and GVSoC
10
10
10
CTRL
DRAM
On-chip
Off-chip
SystemC Models
SystemC
Engine
GVSoC
https://github.com/gvsoc/gvsoc
Synchronization
Interface
Bridge
https://github.com/tukl-msd/DRAMSys

## Slide 11
Scatter
Dialog
Round Shift
Chart: Mesh NoC Dimension
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Thereotical | 8192 | 32768 | 73728 | 131072 | 204800 | 294912 | 401408 | 524288 | 663552 | 819200 | 991232 | 1179648 | 1384448 | 1605632 | 1843200 | 2097152 | 2367488 | 2654208 | 2957312 | 3276800 | 3612672 | 3964928 | 4333568 | 4718592 | 5120000 | 5537792 | 5971968 | 6422528 | 6889472 | 7372800 | 7872512 | 8388608
NoC Model | 8822 | 16502 | 49260 | 98509 | 163958 | 245950 | 344256 | 458957 | 589942 | 737470 | 901210 | 1081534 | 1278142 | 1491034 | 1720438 | 1966286 | 2228342 | 2506942 | 2801854 | 3113150 | 3440831 | 3784794 | 4145242 | 4522174 | 4915390 | 5324990 | 5750974 | 6193242 | 6651994 | 7127230 | 7618752 | 8126669
Chart: Mesh NoC Dimension
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Thereotical | 8192 | 8192 | 8192 | 16384 | 16384 | 24576 | 24576 | 32768 | 32768 | 40960 | 40960 | 49152 | 49152 | 57344 | 57344 | 65536 | 65536 | 73728 | 73728 | 81920 | 81920 | 90112 | 90112 | 98304 | 98304 | 106496 | 106496 | 114688 | 114688 | 122880 | 122880 | 131072
NoC Model | 8834 | 8733 | 8859 | 16600 | 16501 | 24805 | 24790 | 32988 | 32889 | 41185 | 41193 | 49387 | 49377 | 57599 | 57471 | 65770 | 65670 | 73969 | 73975 | 82157 | 82089 | 90357 | 90358 | 98543 | 98543 | 106739 | 106747 | 114943 | 114943 | 123123 | 123127 | 133127
Chart: Mesh NoC Dimension
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Thereotical | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192
NoC Model | 8834 | 8734 | 8858 | 8848 | 8825 | 8932 | 8849 | 8879 | 8903 | 9044 | 8993 | 9132 | 9182 | 9138 | 9185 | 9226 | 9311 | 9492 | 9551 | 9644 | 9627 | 9703 | 9797 | 9980 | 10078 | 10180 | 10279 | 10299 | 10415 | 10628 | 10645 | 10746
M1-WP1: High-Level Simulation Model – Develop Component
Develop Key Components in GVSoC Simulator:
  RedMule – RTL Reference https://github.com/pulp-platform/redmule
  iDMA – RTL Reference https://github.com/pulp-platform/iDMA
  NoC – RTL Reference https://github.com/pulp-platform/FlooNoC
Model Calibration
  RedMule is calibrated with RTL simulation
    runtime deviation 0.17%
  iDMA + NoC model calibration
    3 NoC traffic patterns + static XY routing algorithm
    Compare with the theoretical runtime
    Generally consistent with the theoretical curve

## Slide 12
M1-WP1: High-Level Simulation Model – SoftHier System
Core 0
Core 0
…
Core n
RedMule
iDMA
I $
TCDM (Multi-banked L1)
CTRL
REG
Interconnect
To DATA NoC Router
To SYNC NoC Router
TE Cluster
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
HBM
HBM
HBM
HBM
R
R
Data NoC Router
Sync NoC Router
Fully Parameterizable through Configuration File:
  System configuration
    #Clusters (#row, #column)
    NoC link data width
    #HBM channels and placement on 4 edges
  Cluster configuration
    #Snitch cores
    #TCDM banks, bank data width
    Total TCDM size
    RedMule CE array (height, width, CE pipeline stage)
    iDMA burst length, #outstanding burst
Simulation Assumption
  Cluster instruction cache are large enough and the binary are preloaded at simulation start point

## Slide 13
M1-WP1: High-Level Simulation Model – Open Source
Prepared Hardware Abstract Layer APIs
  Cluster and core position
  Cluster TCDM and HBM address calculation
  Inter- and intra-cluster synchronization
  iDMA and RedMule APIs
Simulator Open-Sourced on GitHub
  Complete SoftHier system model
  Complete software stack
  Getting started tutorial
  Example binaries for execution
https://github.com/gvsoc/gvsoc/tree/soft_hier_release

## Slide 14
M2-WP1: PPA Estimation
Initial Synthesis and PnR Trial
  Thanks to Tim's and Thomas's work on a reduced RTL version of the SoftHier system
  RedMule is not included, focusing on the area and power of iDMA and NoC
  Synthesis and PnR in GLOBALFOUNDRIES’ 12nm FinFET technology, at the typical corner (0.8V, 25°C)
  NoC router with narrow 64b + wide 512b link data width
  Timing: SoC frequency of 1.14 GHz reached
  iDMA per cluster
    Area: 297 kGE (5.3%), Power: 6.3 mW (4.9%)
  NoC router per cluster
    Area: 196 kGE (3.5%), Power: 7.3 mW (5.7%)

## Slide 15
First-Year Milestones Reached
M1-WP1: The Banshee GVSoC open-source simulator will be enhanced to support tensor operators and KiloPE tensor units as well as multiple TEs. Baseline performance models will be added. This simulator will be released to WP2 to help SW development and performance estimation
M2-WP1: A first set of synthesis trials will be run on DMAs and interconnects to estimate cost and performance of the first version of hardware and provide the key components for system-level PPA assessment

## Slide 16
Looking forward to Second-Year Work Package
Architectural Optimization, Tuning, and Microkernels Benchmarking (M3-WP1)
  The data motion engines, the interconnect, and memory endpoints will be tuned and optimized to facilitate programing and boost performance.
  The proposed hardware enhancements will be prototyped, and their performance benefits will be assessed with microkernels
  Hardware costs of the enhancements will be closely monitored to ensure that efficiency remains highly competitive with cache-based techniques, both in terms of system performance and energy efficiency.
Benchmarking on hardware-software integration between the two WPs (M4-WP1-WP2)
  Demonstrating targeted transformations to optimize and streamline performance for CLOUDSC cloud microphysics scheme and the LULESH hydrodynamics solver as well as ML applications.
  Detailed performance study with different application configurations and comparing various workflow options. For Ascend, we will aim at mapping Deep Learning kernels such as Transformer Decoders.
  Open-source release hardware RTL, new version of high-level simulator, software tools and benchmark applications
[1] Riedel, Samuel, et al. "Banshee: A fast LLVM-based RISC-V binary translator." 2021 IEEE/ACM International Conference On Computer Aided Design (ICCAD). IEEE, 2021.

## Slide 17
Weight
Input
Output
Cluster00
Cluster01
Cluster02
Cluster03
Cluster10
Cluster11
Cluster12
Cluster13
Cluster20
Cluster21
Cluster22
Cluster23
Cluster30
Cluster31
Cluster32
Cluster33
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
HBM
Input
No Inter-Cluster L1 Communication
  Each clusters take care of different output tiles.
  iDMA transfers input matrix tile + weight matrix tile from HBM
  No inter-cluster tile reuses
Run Ahead into M3-WP1-- GEMM Dataflow Mapping

## Slide 18
Weight
Output
Input
Cluster00
Cluster01
Cluster02
Cluster03
Cluster10
Cluster11
Cluster12
Cluster13
Cluster20
Cluster21
Cluster22
Cluster23
Cluster30
Cluster31
Cluster32
Cluster33
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
I00
I01
I10
I11
I02
I03
I12
I13
I20
I21
I30
I31
I22
I23
I32
I33
W00
W01
W10
W11
W02
W03
W12
W13
W20
W21
W30
W31
W22
W23
W32
W33
O00
O01
O10
O11
O02
O03
O12
O13
O20
O21
O30
O31
O22
O23
O32
O33
HBM
Leverage Inter-Cluster L1 Communication
  Reuse tiles, reduce HBM accesses, save BW limitation
  Need “smart” tile mapping and scheduling
Run Ahead into M3-WP1 -- GEMM Dataflow Mapping

## Slide 19
Run Ahead into M3-WP1 -- GEMM Dataflow Mapping
An example solution of inter-cluster dataflow for large GEMM.

## Slide 20
Chart: Compute Utilization
| 10KB | 40KB | 160KB | 640KB | 2.56MB | 10.24MB
4x4 Clusters----Enable Cluster Comm | 0.01061 | 0.082902 | 0.47862 | 0.80705 | 0.98997 | 0.99874
4x4 Clusters----No Cluster Comm | 0.010283 | 0.075228 | 0.29249 | 0.53434 | 0.80334 | 0.89668
8x8 Clusters----Enable Cluster Comm | 0.010566 | 0.081064 | 0.45689 | 0.75535 | 0.92451 | 0.99872
8x8 Clusters----No Cluster Comm | 0.01086 | 0.072997 | 0.1744 | 0.31813 | 0.59937 | 0.90131
16x16 Clusters--Enable Cluster Comm | 0.010387 | 0.075919 | 0.438 | 0.72391 | 0.87705 | 0.9649
16x16 Clusters--No Cluster Comm | 0.010834 | 0.043937 | 0.091133 | 0.16759 | 0.31612 | 0.61968
TCDM Size in Cluster:
Max Tile Dimension: 32 64 128 256 512 1024
Benchmark GEMM
  16384 x 16384 x 16384
  GEMM data type = FP16
  8 TFLOPs RedMule per cluster
  NoC link data width = 1024b
Scale-out SoftHier System
  4x4 Clusters + 16 HBM2E channels
  8x8 Clusters + 32 HBM2E channels
  16x16 Clusters + 64 HBM2E channels
    2048 TFLOPS @FP16
    3.2 TB/s HBM BW
Key Results: Enabling cluster-to-cluster comm is scalable, which reduces off-chip traffic and no need to increase L1 size for better compute utilization when scaling out
Run Ahead into M3-WP1 -- GEMM Dataflow Mapping

## Slide 21
Run Ahead into M3-WP1 -- GEMM Dataflow Mapping
Explore More GEMM Dataflow
  1. On-chip shuffling – double buffering {compute, on-chip transfer}
  2. On-chip shuffling – triple buffering {compute, on-chip transfer, off-chip transfer}
  3. Systolic-wise streaming – double buffering {compute, neighbor node transfer}
Benchmark GEMM
  16384 x 16384 x 16384
  GEMM data type = FP16
  8 TFLOPs RedMule, 1MB L1 per Cluster
  8x8 Clusters + 32 HBM2E channels
Result
  Systolic streaming is better
    Require narrower NoC link data width
Chart: NoC Link DateWidth (Bits)
| 512 | 1024
OnChip Shuffle [double buffer] | 0.50585 | 0.56215
OnChip Shuffle [triple buffer] | 0.45776 | 0.79024
Systolic Stream [double buffer] | 0.84508 | 0.83825
1
2
3

## Slide 22
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
RM
Many Clusters with Small RedMule vs. Few Clusters with Big RedMule
  Invariant Parameters During SoftHier System Transformation:
    Total compute power
    Total L1 area budget
    NoC link width
    Total HBM BW
Run Ahead into M3-WP1 -- Architecture Design Exploration

## Slide 23
Chart: SoftHier Configuration
| a | b | c | d | e
L1 BW = RedMule Required BW | 0.21973 | 0.43553 | 0.69593 | 0.62253 | 0.58649
L1 BW = 2x RedMule Required BW | 0.21975 | 0.4367 | 0.84508 | 0.81298 | 0.71833
Benchmark GEMM
  16384 x 16384 x 16384
  Systolic-like inter-cluster tile stream
Result
  Few clusters with big RedMule
    Limited by NoC BW (if it can not scale)
    Other potential limitations
      RedMule may not scale
      L1 TCDM BW may not scale
      Less flexible for application with small GEMM
  Many clusters with small RedMule
    Small L1-> Shorter GEMM steps -> More sync needed
    Many cluster -> Each sync costs more time
Chart: Runtime Breakdown
| e | d | c | b | a
RedMule runtime | 38448 | 37441 | 37435 | 37131 | 37050
Wait for iDMA | 0 | 0 | 0 | 37129 | 111751
Sync Overhead | 7169 | 2865 | 1340 | 775 | 311
Sync-bound
NoC BW-bound
Run Ahead into M3-WP1 -- Architecture Design Exploration

## Slide 24
Run Ahead into M3-WP1 -- Multi-Head Attention Mapping
Proposed Dataflow Schedule of MHA on SoftHier (FlattenAttention)
  We leverage all-cluster L1 for single head attention – Minimize I/O complexity
  We introduce performance model of specific accelerators in each cluster to complete MHA
    Vector engine for SoftMax operations (max(V), sum(V), sub(V,s), exp(V), div(V,a))
    Matrix transpose engine for transposition of (K -> KT)
    Virtually enable collective operations on NoC -- estimate runtime for NoC collective operations
Benchmark & Results
  16x16 Clusters(8TFLOPS, 256kB L1), 2TB/s HBM
  One layer MHA of Llama3-70B (seq=4K, batch=8)
  Efficient collective operation support on NoC is essential
    3x speedup to baseline
Total Runtime(ms) | 
Baseline: Flash Attention for Each Head on Each Cluster | 14.4
Flatten Attention (w/o NoC collective) | 17.7
Flatten Attention (w/ NoC collective) | 4.6

## Slide 25
Looking Forward – Exploration Directions
HW Enhancement
  NoC collective operation support solutions (RTL + GVSoC)
  Enable iDMA for on-the-fly matrix transposition
Tracking the HW Cost
  Setting up area and timing models for key components: RedMule, iDMA, FlooNoC
Design Space Exploration (LLM-Oriented)
  A template code for end-to-end LLM inference/training workload
  Architecture design space exploration for the SoftHier system
    Finding the optimal configuration for a set of LLM model and workloads