## Slide 1: QuantSparse 3D Biweekly 2025-05-06
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  Spatz: Multi-level N:M sparsity handling, RTL
  Deployment: SoftHier Runtime Memory Allocation Support
  3D Chiplet Interconnection: Literature Review
Timeline
Discussion

## Slide 3: Spatz N:M Sparsity Handling - VLSU
SpDotp
  No data reuse in dense activation vector  Effective activation elements are gathered at VLSU level
  Standard RVV instruction support (vloxei.v)
  No Vreg overhead to store ineffective activation elements
  Theoretical max. VPU utilization: ~50%
    The effective VLSU-to-L1 bandwidth is halved when loading activation
RTL update
  Completed coalescing strides in the commit stage and ongoing functional verification

## Slide 4: Spatz N:M Sparsity Handling - Vreg
SpMV
  Reuses the dense activation vector across multiple weight matrix rows
    Gathering at VLSU is inefficient
  Entire input vector is loaded into Vregs  Effective activation elements are gathered within Vreg using vrgather.vv
  Additional VReg storage is required
  Theoretical VPU utilization 75%~90%
    Efficient gather operation
  Applicable for SpMM
RTL Update
  Finished first-version implementation, functional verification ongoing

## Slide 5: Memory Allocation Runtime in SoftHier
Original memory management in SoftHier
  Static memory allocation for both HBM and L1
  Assume input/output addresses are unchanged throughout the program  Unsustainable when deploying networks beyond multiple layers
Added runtime libraries
  Dynamic memory allocation for HBM and L1
    Per-cluster, privately accessed L1 allocator
    Per-system, shared HBM allocator
Ongoing extensions
  Globally accessed allocation data structure  inter-cluster block DMA operations
https://github.com/gvsoc/gvsoc/tree/soft_hier_release(#91)

## Slide 6: TSMC InFO_SoW[1] Example: Tesla Dojo D1[2]
A mesh of individual units connected by a high-speed 2D fabric
Each individual unit has:
  1.25MB SRAM scratchpad
    Gather engine at 8B and 16B granularity
  4 superscalar CPU cores with 64B SIMD unit and 8x8x4 matrix multiply units
    Customized ML formats (CPF8/16)
    Customized ML instructions (gather operands, tensor transpose, compressed operands expansion)
  Independent NoC router
    Direct SRAM connection, one read and one write packet per cycle
    Block level DMA operations

## Slide 7: TSMC InFO_SoW[1] Example: Tesla Dojo D1[2]
Dojo D1 die manufactured in TSMC 7nm
  354 Dojo processing nodes per die
  440 MB on-chip SRAM
  362 TFlops BF16/CFP8, 22 TFlops FP32 @2GHz
5x5 array of D1 chips per training tile
  Packaged with TSMC InFO_SoW
    low latency chip-to-chip communication, high bandwidth density
    enabled chiplet-based design for greater cost saving and design flexibility
Potential wafer-scale integration with TSMC-CoSoW[3] by 2027

## Slide 8: 3D-Chiplet Interconnection: Literature Review
How do we best interconnect stacks through the interposer?
Feng et al[4] enable high-radix interconnect between chiplets:
  Based on minus-first routing (MFR)[5] with multiple improvements
  Groups, interleaves interface nodes
  Supports nD mesh, dragonfly, hypercube
Notably better latency, throughput
  High radices scale better with #chiplets
  Notable reduction in energy, esp. off-chip
  Interleaved interface nodes help

## Slide 9: Timeline
Year 1 2026-02
Project Start 2025-02
Literature Review 2025-04
  Literature review on sparsity and quantization format supported on SoA platforms
  Multi-granularity sparsity handling
  Proposed Spatz-based multi-cluster architecture; Literature review on quantization handling
  Spatz GVSoC model VLSU port extension; Start NoC packing scheme; Initial discussion on 3D chiplet integration
  Spatz multi-level N:M sparsity handling; SoftHier memory allocation runtime; Discussion on 3D integration
  Customized data format for MX-like quantization and N:M structured sparsity
  Customized ISA support in Spatz GVSoC model
  Next step:

## Slide 10: References
[1] C. Shu-Rong, et al. "InFO_SoW (system-on-wafer) for high performance computing." IEEE ECTC, 2020.
[2] T. Emil, et al. "Dojo: The microarchitecture of tesla’s exa-scale computer." IEEE HSC, 2022.
[3] H. Yu-Chen, et al. "CoWoS architecture evolution for next generation HPC on 2.5 D system in package." IEEE ECTC, 2023.
[4] Y. Feng et al., “A Scalable Methodology for Designing Efficient Interconnection Network of Chiplets,” IEEE HPCA, 2023
[5] D. Xiang et al., “Deadlock-Free Broadcast Routing in Dragonfly Networks without Virtual Channels,” IEEE TPDS, 2023

## Slide 11: Backup: Handle at VLSU
Theoretical max. VPU utilization: 50%
Theoretical max. VPU utilization: 50%
Granularity mismatch 
Theoretical max. VPU utilization: 33%
Lower precision weights 
Theoretical max. VPU utilization: ~75-100%
Lower precision weights 
Theoretical max. VPU utilization: ~50%
  ~50% upper-bound VPU utilization limited by VLSU-to-L1 effective bandwidth
  Design trade-off at L1 memory bankwidth

## Slide 12: Backup: Handle at VReg
Inefficient if no reuse in the dense input tensor
VReg overhead to store the gathered input elements
Max. VPU utilization: ~33%
Input tensor is reused over multiple iterations
The gathering operation becomes the bottleneck
Max. VPU utilization: ~50%
The gathering operation’s efficiency
depends on the VSLIDE unit implementation (e.g. port reuse)
Max. VPU utilization: ~75-100%