## Slide 1: QuantSparse 3D Biweekly 2025-07-22
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Progress Recap
  WP1
  Software emulation on SpMM with RVV instructions
  Custom widening index instructions in Spatz GVSoC model
  SpMM kernel implementation with vfwx_.vf instructions

## Slide 3: Agenda
Progress Update
  Spatz N:M sparsity format
    Baseline: Dense vs. sparse (2:4) FP8 MatMul
    Optimization: Loop unroll, VRF prefill
    Performance benchmark, insights
Timeline
Discussion

## Slide 4: Recap: Dense MatMul (Gustav)
Middle Loop
Outer Loop
Inner Loop

## Slide 5: Baseline Benchmark: Dense MatMul
VPU utilization increases with larger P dimension due to longer Vl
VPU utilization is constrained by WAR dependency

## Slide 6: Recap: SpMM Software Emulation (Gustav)
~50% instructions are used for config + scatter/gather
Inner Loop
Index generation is required

## Slide 7: Baseline Benchmark: SpMM Software Emulation
Vectors with >256 elements cannot be processed in one iteration, due to the 8-bit index constraint
Performs poorly due to software index translation and reliance on VLSU for scatter/gather

## Slide 8: Recap: SpMM Custom Instruction (Gustav)
Scatter/Gather in VRF
Merged index translation
No configuration overhead

## Slide 9: Baseline Benchmark: SpMM Custom Instructions
Timing model:
  vfw_.vf instructions are aligned with RTL implementation. For FP8 inputs, 1 cycle latency
  vfwx_.vf instructions are estimated.
  VREG-based scatter/gather, which effectively halves the VREG-to-VPU bandwidth under 2:4 sparsity  Latency is modeled as double that of regular vfw_.vf instructions

## Slide 10: Baseline Benchmark: SpMM Custom Instructions
Larger control instruction overhead for indices
Additional runtime for loading index vector
Reduced runtime for computation

## Slide 11: Optimization: Loop Unroll
Mitigate control instruction overhead impacts
Increased data reuse

## Slide 12: Optimization: VREG Preload
Removed data compute-load dependency
Unroll
Preload

## Slide 13: Speed Up
Results:
  Up to 1.60x speedup with long vl
  Lower performance with shorter vl, as a result of higher control overhead (address calculation)  Post-Incrementing vector Load & Store Instructions
Limitations
  No vector chaining support in the current Spatz GVSoC model
Work in progress
  Add kernel for activation sparsity handling
  MX-format combined handling
https://github.com/gvsoc/gvsoc/tree/soft_hier_release(#137)

## Slide 14: Progress Update
  WP1
  SpMM kernel implementation, optimization, and benchmark with vfwx_.vf instructions