## Slide 1: QuantSparse 3D Biweekly 2025-09-10
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Progress Recap
  WP1
  Structured sparsity handling wrap-up

## Slide 3: Agenda
Progress Update
  Block quantization: Microscaling (MX) format
    OCP Microscaling Formats (MX) Specification
    FPU DOTP datapath
  MX format handling
    FPU MXDOTP datapath
    Quantization-axis consideration
  Joint Handling of MX and N:M Structured Sparsity
    Sparsification, quantization-axis joint consideration
Timeline
Discussion

## Slide 4: OCP Microscaling Format (MX) Specification[1]
MX-compliant format is characterized by:
  Scale (X): data type & encoding
  Private elements (): data type & encoding
  Scaling block size (k)
Bit-width representations
  Shared scale encoding (w)
  Private element encoding (d)
8-bit (E8M0)
8-bit (E5M2 or E4M3)
32

## Slide 5: OCP Microscaling Format (MX) Specification[1]
Basic operations
  Dot product of two MX-blocks
    A and B may use different data types
    The internal precision is implementation-defined
  General dot product of two MX-vectors
    Accumulator (C) should be Float32
Dot Product
General Dot Product

## Slide 6: Spatz4 Datapath
Vector processing unit (VPU)
  Comprises four 64-bit FPUs operating in parallel
  Connected via a 256-bit interconnect to VREG
FPU datapath comprises operations groups
  N:M format handling leverages the ADDMUL operation group

## Slide 7: Spatz4 Datapath
Vector processing unit (VPU)
  Comprises four 64-bit FPUs operating in parallel
  Connected via a 256-bit interconnect to VREG
FPU datapath comprises operations groups
  N:M format handling leverages the ADDMUL operation group
  MX specification: FP8 input elements, FP32 accumulator  widening instruction required
  Effective throughput is halved (4x FP8 inputs per cycle)
Per FPU workload

## Slide 8: Spatz4 Datapath
DOTP operation group
  2x throughput compared with ADDMUL
  Low latency depends on the number of pipeline stages
  Per FPU operates on an inner-product dataflow
Per FPU workload

## Slide 9: Spatz4 Datapath
DOTP operation group
  2x throughput compared with ADDMUL
  Low latency depends on the number of pipeline stages
  Per FPU operates on an inner-product dataflow
  Per Spatz operates on a mixture of inner-product/Gustav dataflow
Per Spatz workload

## Slide 10: MXDOTP[2]: RV ISA Extension for MX Dot Products
MXDOTP operation group
  Datapath is integrated into the FPU of the Snitch Cluster as an additional operation group
  Computes the dot product between vectors of eight FP8 elements
  Throughput: one FP32 result per cycle
Implementation and area analysis
  Synthesize, PnR with GF 12nm FinFET
  1.09GHz @ TT/0.8V/25°C, with three pipeline stages, without introducing new critical paths
  26 kGE per MXDOTP datapath, 17% of FPU area

## Slide 11: GEMM Quantization-axis Consideration
Rows of the weight matrix
  Scales need to be applied directly after MUL  duplicated logic
  High bit-count (FP32) adder tree  large area footprint

## Slide 12: GEMM Quantization-axis Consideration
Columns of the weight matrix
  Low-precision adder tree  area efficiency
  The scales only need to be calculated and applied at the final stage

## Slide 13: VMXDOTP

## Slide 14: VMXDOTP

## Slide 15: GEMM Sparsification-axis Consideration
Orthogonal to the MX blocks
  Columns of weight elements utilize distinct shared scales
  An additional shuffling stage to group elements with the same scales together
  Dynamic MAC unit linkage relies on N:M indices
  Separate logic blocks for applying scales and accumulation
   Difficult to scale for various N:M format and MX precisions
2:4 format as an example

## Slide 16: GEMM Sparsification-axis Consideration
Aligned to the MX blocks
  Columns of weight elements share the same MX scales
  An additional gathering stage to group effective activation elements (same as the discussion in the N:M format handling)
  MXDOTP datapath remains unchanged
  Compatible with both N:M and MX formarts
2:4 format as an example

## Slide 17: Takeaways
Gustavson-based dataflow with ADDMUL operation group
  Lower throughput with widening instructions
  An additional conversion step (FP8FP16) is required to align with the OCP MX specification
  Compatible with high-sparse activation tensors (i.e., top-k, top-theta)
Mixed-type dataflow with MXDOTP operation group
  Inner product per FPU
  2x throughput increment compared with ADDMUL options
  Weight matrix column-wise quantization is required for area and energy efficiency
  Sparsification is aligned with the quantization direction for scalability

## Slide 18: Roadmap
Model compression techniques revisit
  Pruning
    Weight structured/unstructured pruning
    Activation (token) unstructured pruning
    Attention (KV pruning)
  Low-precision quantization
    Block quantization with MX format – Outlier handling
    Vector quantization*
Proposed handling mechanism
Discussion

## Slide 19: Weight Pruning
Structured pruning
  Strictly removing structured sets of parameters
  SoA methods[1][2]: 50%-75% sparsity rate
Unstructured pruning
  Arbitrary patterns of sparsification for parameters
  SoA methods[3]: 90% sparsity rate without performance drop

## Slide 20: Activation Pruning
Unstructured pruning
  Dynamically detect and zero out unimportant activations at run-time
  In Transformer inference, the mainstream branch of activation pruning is token pruning[4][5]
    Detects and drops less important tokens in each Transformer layer from the rest of the inference
    Result: Reduced sequence length  No impact on PE handling with inner-product or Gustav-based dataflow

## Slide 21: Attention Pruning (Sparse Attention)
Unstructured pruning
  Leverage the dynamic sparsity patterns of the attention score activations
  Many combinations of query and key tokens are not semantically meaningful[6][7]
    Keep the Top-k largest attention score activations (unstructured attention score)
    Keep the corresponding rows of the Value matrix (row-wise structured sparsity)

## Slide 22: Low-precision quantization
Block quantization with MX formats
  Uniform quantization: splits the floating-point domain into evenly spaced intervals and maps each interval into a single value  activation outliers[8]
  Non-uniform quantization: no requirement for the intervals to be evenly spaced  circumvent the activation outlier issue[9]
    MX format is block-level uniform, global non-uniform quantization
    Vector quantization(VQ) is non-uniform quantization
  Weight outliers still need to be handled
    The majority of the weight elements can be compressed to 3-4 bits, while less than 1% outliers (unstructured sparse) are stored in FP16[10]

## Slide 23: Proposed Solution: Sparsity Handling
Dense-Dense
  Gustav-based dataflow with ADDMUL operation group
  Inner-product dataflow with ADDMUL operation group requires a reduction stage

## Slide 24: Proposed Solution: Sparsity Handling
Dense-Structured
  Gustav-based dataflow with ADDMUL operation group
  Utilize the indexed-macc operation
    Remove the index translation between the N:M format and RVV spec
    Modeled in GVSoC, with one important insight  Efficient VRF gather operation required

## Slide 25: Proposed Solution: Sparsity Handling
Dense-Unstructured
  SSSR-like support
  Assume MatMul (1xExP) with a 90% sparsity rate in the weight matrix, with Snitch+SSSR
    , Computational throughput
  Comparing with a single Spatz4 with dense equivalent computation
    , Computational throughput
  Brief insight: We need at least 2 SSSR-like support to achieve actual speedup

## Slide 26: Proposed Solution: Sparsity Handling
Current SSSR streaming limitation
  The streaming units work on L1 bank-width granularity  underutilized bandwidth
  Extend streaming units with lower control granularity, L1-to-SSSR gather operation
Potential SSSR integration
  (P1) Heterogeneous cluster: Spatz and Snitch + SSSR, unstructured workload map to SSSR
  (P2) Vector streaming processor: reformulate Spatz VLSU and VRF
Notes: address generate replication + chaining, bypass the VRF

## Slide 27: Proposed Solution: Sparsity Handling
Sparse attention
  Fundamentally, still a ‘dense’ GEMV
  PE level, still handled by scalar-vector multiplication, with Gustav-based dataflow
  The vectors of Value matrix should be loaded according to the top-k attention score indices  Vector-level loading/indirect streaming

## Slide 28: Proposed Solution: Sparsity + Block Quantization
MX Dense-Dense (ignoring the outliers)
  Per FPU inner-product dataflow, per Spatz mixed (inner+Gustav) dataflow
  Row-wise quantized activation, column-wise quantized weight
  Highlight the requirement for online MX quantization (FP32  MXFP8)
Notes: memory load section speed up
not focus to much the computation speed up from MX

## Slide 29: Proposed Solution: Sparsity + Block Quantization
MX Dense-Structured (ignoring the outliers)
  The pruning direction needs to align with the quantization direction
  MXDOTP operation group can be reused without modification
  Gather operation support in VRF

## Slide 30: Proposed Solution: Sparsity + Block Quantization
Outlier handling
  1% weight outliers stored as FP16, when the majority of the weight elements are compressed to 3-4 bits (MXFP4)
    Should be calculated seperately
  Assume MatMul (1xExP):
    Use Snitch to handle outliers: , Computational throughput (FP16)
    Use Spatz for dense comp.: , Computational throughput (MXFP4)
    Need one additional SSSR-like support, so that unstructured computation is not the performance bottleneck

## Slide 31: Proposed Solution: Sparsity + Block Quantization
Sparse Attention + MX
  Value matrix is MX-quantized after the KQV Gen stage, stored back in HBM
  Top-k selection determines rows of the Value matrix load back to L1  Dequantize
  Computation with FP16, much less data movement overhead
Notes: quantizagtion after transaction does not make sense
dont bring in the unnecessary data (latency - throughput tradeoff)
we drop the
We just quantized value matrix for transfer, load back and dequantized it (good idea)
memory save is the key!!!

## Slide 32: Roadmap

## Slide 33: Progress Update
  WP1
  MX, N:M format co-consideration

## Slide 34: References
[1] Bita, Rouhani, et. al., “OCP Microscaling Formats (MX) Specification, Version 1.0.” [Online]. Available: https://www.opencompute.org/documents/ocp-microscaling-formats-mx-v1-0-spec-final-pdf
[2] İslamoğlu, Gamze, et al. "MXDOTP: A RISC-V ISA Extension for Enabling Microscaling (MX) Floating-Point Dot Products." arXiv preprint arXiv:2505.13159 (2025).

## Slide 35: References
[1] Xia, M, et al. "Structured pruning learns compact and accurate models." arXiv preprint arXiv:2204.00408 (2022).
[2] Sun, Mingjie, et al. "A simple and effective pruning approach for large language models." arXiv preprint arXiv:2306.11695 (2023).
[3] Kurtic, Eldar, et al. "The optimal bert surgeon: Scalable and accurate second-order pruning for large language models." arXiv preprint arXiv:2203.07259 (2022).
[4] Goyal, Saurabh, et al. "Power-bert: Accelerating bert inference via progressive word-vector elimination." International Conference on Machine Learning. PMLR, 2020.
[5] Kim, Gyuwan, and Kyunghyun Cho. "Length-adaptive transformer: Train once with length drop, use anytime with search." arXiv preprint arXiv:2010.07003 (2020).
[6] Gupta, Ankit, et al. "Memory-efficient Transformers via Top-$ k $ Attention." arXiv preprint arXiv:2106.06899 (2021).
[7] Berestizshevsky, Konstantin, et al. "Top-theta attention: Sparsifying transformers by compensated thresholding." arXiv preprint arXiv:2502.08363 (2025).
[8] Kovaleva, Olga, et al. "BERT busters: Outlier dimensions that disrupt transformers." arXiv preprint arXiv:2105.06990 (2021).
[9] Zadeh, Ali Hadi, et al. "Gobo: Quantizing attention-based nlp models for low latency and energy efficient inference." 2020 53rd Annual IEEE/ACM International Symposium on Microarchitecture (MICRO). IEEE, 2020.
[10] Dettmers, Tim, et al. "Spqr: A sparse-quantized representation for near-lossless llm weight compression." arXiv preprint arXiv:2306.03078 (2023).