## Slide 1: QuantSparse 3D Biweekly 2025-09-24
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Progress Recap
  WP1
  Roadmap on efficient scatter/gather operation and unstructured data structure streaming

## Slide 3: Agenda
Progress Update
  Spatz VRF architecture
  Efficient scatter/gather operation
    Existing VSLDU-based design and limitations
    Proposal 1: VRF reformulation
    Proposal 2: Buffer-based design
  Overhead analysis
Timeline
Discussion

## Slide 4: Spatz VRF Architecture
Spatz VRF is implemented as a multi-banked, multi-ported, latch-based standard cell memory SCM
  32 VLENB bytes of the VRF are divided into four banks
  three read ports and one write port (3R1W)  Provides enough bandwidth for executing vfmacc.vv instruction

## Slide 5: Spatz VRF Architecture
Spatz VRF is implemented as a multi-banked, multi-ported, latch-based standard cell memory (SCM)
  32 VLENB bytes of the VRF are divided into four banks
  three read ports and one write port (3R1W)  Provides enough bandwidth for executing vfmacc.vv instruction
  Each with VLENB/2 byte width
In SoftHier, Spatz VLENB = 512 (i.e., 16 KiB VRF)

## Slide 6: Spatz VRF Architecture
Spatz VRF is implemented as a multi-banked, multi-ported, latch-based standard cell memory (SCM)
  32 VLENB bytes of the VRF are divided into four banks
  three read ports and one write port (3R1W)  Provides enough bandwidth for executing vfmacc.vv instruction
  Each with VLENB/2 byte width
In SoftHier, Spatz VLENB = 512 (i.e., 16 KiB VRF)
Spatz has three function units:
  VAU: Vector Arithmetic Unit
  VLSU: Vector Load/Store Unit
  VSLDU: Vector Slides Unit

## Slide 7: Sc/Ga Operation: Existing VSLDU-based design
Extended VSLDU with an additional port for indices
  Support native N:M formats
Limitations:
  Throughput bottleneck: With a 50% sparsity rate, Cycle 1 produces the upper-half gathered output, and Cycle 2 produces the lower-half
  Lack of streaming: VSLDU gathers a vector from VRF, writes it back, and requires an additional read for arithmetic.
Insights:
  Asymmetrical bandwidth required to feed VAU at full utilization
  Streamlined Sc/Ga operation with arithmetic

## Slide 8: Design Requirements
Based on Spatz:
  Asymmetrical bandwidth required to feed VAU at full utilization
  Streamlined Sc/Ga operation with arithmetic
  Support up to 75% sparsity ratio (e.g., 1:4), aligned with SoA studies  Gather: input bandwidth 4× the output port Scatter: output bandwidth 4× the input port

## Slide 9: Inserting Sc/Ga Datapath into VRF
Gather effective elements from VRF
  1024-bit input, 256-bit output datapath
  r2 port of all banks will be occupied @ 75% sparsity rate  VLSU port can be re-routed to r1 XBar

## Slide 10: Inserting Sc/Ga Datapath into VRF
Gather effective elements from VRF
  1024-bit input, 256-bit output datapath
  r2 port of all banks will be occupied @ 75% sparsity rate  VLSU port can be re-routed to r1 XBar
Scatter effective elements to VRF
  256-bit input, 1024-bit output datapath
  w port of all banks will be occupied @ 75% sparsity rate  VLSU and VSLDU cannot write back to VRF (port conflict)

## Slide 11: Proposal 1: VRF Reformulation
To resolve the scattered-write port conflict
  Double the number of banks 4  8

## Slide 12: Proposal 1: VRF Reformulation
To resolve the scattered-write port conflict
  Double the number of banks 4  8
The gather datapath steers to the upper or lower four banks
  Depends on VRF mapping

## Slide 13: Proposal 1: VRF Reformulation
To resolve the scattered-write port conflict
  Double the number of banks 4  8
The gather datapath steers to the upper or lower four banks
  Depends on VRF mapping
Expanded crossbar
  For doubled memory banks and the additional gather datapath

## Slide 14: Proposal 1: VRF Reformulation
To resolve the scattered-write port conflict
  Double the number of banks 4  8
The gather datapath steers to the upper or lower four banks
  Depends on VRF mapping
Expanded crossbar
  For doubled memory banks and the additional gather datapath
Additional crossbar for VAU routing
  Gustav: gather for accumulated outputs (vd)
  Inner-product: gather for input activations (vs2)

## Slide 15: Proposal 1: VRF Reformulation
To resolve the scattered-write port conflict
  Double the number of banks 4  8
The gather datapath steers to the upper or lower four banks
  Depends on VRF mapping
Expanded crossbar
  For doubled memory banks and the additional gather datapath
Additional crossbar for VAU routing
  Gustav: gather for accumulated outputs (vd)
  Inner-product: gather for input activations (vs2)
Similar architecture for the w datapath

## Slide 16: Proposal 1: VRF Reformulation
Hardware overhead analysis
  Sixteen 256-bit (1x2) and two 1024-bit (1x2) MUX/DEMUX from banks to the Sc/Ga datapath
  r0/r1 crossbar: 256-bit (4x2) 256-bit (8x2); r2 crossbar: 256-bit (4x2) 256-bit (9x2); w crossbar: .256-bit (3x4)  256-bit (3x9)
  VAU routing: 256-bit (2x2) crossbar
  Scatter/Gather datapath

## Slide 17: Proposal 2: Buffer-based Design
VRF remains unchanged

## Slide 18: Proposal 2: Buffer-based Design
VRF remains unchanged
The scatter/gather datapath and buffer are implemented along the VAU
  A 1024-bit 1R1W interface is required for the buffer

## Slide 19: Proposal 2: Buffer-based Design
VRF remains unchanged
The scatter/gather datapath and buffer are implemented along the VAU
  A 1024-bit 1R1W interface is required for the buffer
Similar crossbar structure for VAU routing

## Slide 20: Proposal 2: Buffer-based Design
Hardware overhead analysis
  One 4KiB buffer, assuming to support LMUL=8 accumulation
  One 256-bit (3x2) crossbar and one 256-bit (1x2) MUX
  Scatter/Gather datapath
Energy efficiency consideration
  Avoids the need to activate 4x the banks every cycle into the VRF  saves energy since it does not activate a large VRF
Buffer reuse
  The inserted buffer could be repurposed for no-reuse vector streaming

## Slide 21: Progress Update
  WP1
  Proposal for the efficient scatter/gather operation
  Backend exploration for Proposal 1