## Slide 1: QuantSparse 3D Stage Report
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Model Scaling Outpaces Computing Capability
2.4x/year
1.3x/year
Number of parameters of frontier AI models
Computational throughput of ML hardware
                Modern ML platforms provide massively parallel computing capabilities through system scaling
NVIDIA Blackwell[1]
16,869 Scalar Cores + 528 Tensor Cores
AMD INSTINCT MI355X[2]
16,384 Scalar Cores + 1024 Tensor Cores
Cerebras WSE-3[3]
900,000 Scalar Cores
Google TPU Ironwood[4]
Scale out to 9,216 chips
Massively Parallel Architectures
[1] T. Ajay, et al. "Nvidia blackwell platform: Advancing generative ai and accelerated computing." HCS ‘24.
[2] S. Alan, et al. "AMD InstinctTM MI300 series modular chiplet package–HPC and AI accelerator for exa-class systems." ISSCC ‘24.
[3] I. Lie, Sean. "Cerebras architecture deep dive: First look inside the hw/sw co-design for deep learning: Cerebras systems." HCS ‘22.
[4] J. Norman, et al. "Ironwood: Delivering Best in Class perf, perf/TCO and perf/Watt for Reasoning Model Training and Serving." HCS ‘25.

## Slide 3: Expanding Memory Pressure
KV cache dominates memory usage in long context agentic inference workload
Memory BW growth cannot keep pace with Computing​
High-capacity + High-bandwidth on-chip memory
Google TPU Ironwood
192 GB @ 7.4 TB/s HBM
AMD INSTINCT MI355X
288 GB @ 8 TB/s HBM3e
d-Matrix Corsair[1]
2 GB @ 150 TB/s DIMC
NVIDIA Blackwell
192 GB @ 8 TB/s HBM3e
Advanced Integration
[1] Bhoja, Sudeep. "CORSAIR: An In-Memory Computing Chiplet Architecture for Inference-Time Compute Acceleration." HCS ’25.

## Slide 4: Rising Energy Cost
1.9x/year
1.3x/year
Power requirements of leading AI supercomputers
Energy Efficiency of leading ML hardware
Driven by reducing data movement, computing specialization, and exploiting numerical co-design
Google TPU Ironwood
Systolic array-based dataflow
NVIDIA Blackwell
FP4/FP8 Tensor Cores
d-Matrix Corsair
NPU-style CIM
Tenstorrent Blackhole[1]
Dataflow-aware routing
Algorithm Innovation
Hardware Specialization
[1] BVasiljevic, Jasmina, and Davor Capalija. "Blackhole & tt-metalium: The standalone ai computer and its programming model." HCS ‘24.
Notes: Google TPU (v1–v5 / IronWood): Systolic array-based dataflow minimizes memory access and exploits massive data reuse for MAC operations — a key source of energy savings. → Highlight: “Dataflow specialization to reduce off-chip movement.”
d-Matrix Corsair / NPU-style in-memory compute: The chiplet-based analog compute design moves MAC operations closer to SRAM banks, drastically reducing data transfer energy. → Highlight: “Near-memory compute to minimize energy per operation.”
Tenstorrent Blackhole: Emphasizes dataflow-aware routing and on-chip mesh network optimization for low-latency and energy-efficient transfers.

## Slide 5: QuantSparse 3D Project Objective
  Reduce the energy consumption of large model inference by combining quantization and sparsity techniques to maintain performance under power constraints
WP1: Architectural modeling, simulation, and design of the chiplet architecture
Project Structure (Year 1)
WP2: Multi-chiplet fabrics modeling and software environment for model deployment

## Slide 6: Review of First-Year Work Packages
(WP1) Chiplet architecture and building blocks
  Architectural modeling, simulation, and design of the chiplet architecture, including processing engines, on-chip interconnect, memories, and main memory endpoints (controllers and near/in memory compute units).
  Parameterized RTL models will be built and synthesized on advanced technology models representative of state-of-the-art technologies to assess PPA.
(WP2) System and software design
  Architectural modeling of multi-chiplet fabrics and 3D-stacked memories.
  Software environment for mapping LLM models to the hardware architecture, leveraging open-source environments (PyTorch, TVM, LLVM) and open specifications (ONNX).
  Design space exploration of system configurations using a set of simplified end-to-end models and microkernels, such as autoregressive inference using a KV-cache for long input sequences, also using micro-scaling formats to reduce memory and energy footprints.
Notes: packages

## Slide 7: QuantSparse3D: Model Quantization
Models with billions and trillions of parameters
  E.g., Open AI GPT, Google Gemini, Meta LLaMa
  Challenging to run in cloud and on edge devices
Key challenges:
  These models have massive computational and memory costs
  Complex to deploy and tricky to evaluate
Key opportunities:
  Intuitively, these models are heavily over-parameterized and highly compressible
  We need efficient hardware and software support for “compact” representations
Massive Models are a big deal
  Can we obtain highly-compressed but accurate variants?
  Main research direction: Model Quantization

## Slide 8: The Frontier: Toward Low-Bit, Lossless* Quantization
Zoo of quantization ideas[1]
  Rescaling: SmoothQuant, Base-Q
  Rotation/Permutations: QuaRot, OSTAQuant, DuQuant
  Learned rotations: SpinQuant, FlatQuant
  Outlier preservation: Atom, QUIK
Research mainstream: Post-training quantization compresses LLMs in one-shot
Weight-only quantization is helpful in the memory-bound regime
  What about computational throughput?
Key idea: allows the multiplication to happen in lower precision
  Going sub-8-bit exposes the limits of scalar quantization + fast-moving landscape calls for standardization
  Microscaling (MX) format is emerging as the standard
* Lossless: reducing precision without causing any measurable degradation in model accuracy compared to full-precision.
[1] Lang, Jiedong, Zhehao Guo, and Shuyu Huang. "A comprehensive study on quantization techniques for large language models." 2024 4th International Conference on Artificial Intelligence, Robotics, and Communication (ICAIRC). IEEE, 2024.

## Slide 9: Block Quantization: Microscaling (MX)
  Aggressive low-bit quantization requires both MX and explicit outlier handling Hardware must provide native, decoupled support
OCP MX Specification[1]
MX-compliant format is characterized by:
  Scale (X): data type & encoding
  Private elements (): data type & encoding
  Scaling block size (k)
8-bit (E8M0)
8-bit (E5M2 or E4M3)
32
MX provides higher effective dynamic range than scalar quantization
0.001~1% unstructured outlier overlay[2]
  Different layers demonstrate distinct outlier patterns
  Represented with higher precision
[1] Rouhani, Bita Darvish, et al. "Microscaling data formats for deep learning." arXiv preprint arXiv:2310.10537 (2023).
[2] Park, Jungwoo, et al. "Outlier-Safe Pre-Training for Robust 4-Bit Quantization of Large Language Models." arXiv preprint arXiv:2506.19697 (2025).
Notes: https://ieeexplore.ieee.org/document/10994764?denied=

## Slide 10: QuantSparse3D: Model Pruning
  Coarse-grained pruning reduces macro-level workload, but compute kernels stay dense Handled at graph/compiler level
Large building blocks are removed; computation remains dense inside each kept block
Mixture-of-Expert (MoE) Models
  Pruning removes entire experts, keeping only a small subset active per token
  Requires compiler/runtime support to schedule experts
Layer dropping / block-level pruning
  Remove attention blocks, MLP blocks, or entire layers
Token pruning
  Reduces sequence length but does not change PE datapath
Coarse-Grained Sparsification

## Slide 11: QuantSparse3D: Model Pruning
  Fine-grained pruning dictates hardware datapath changes, specialized sparse-matmul units, and dedicated memory operations
Individual elements or small groups are removed
Weight Pruning
  Structured: Strictly removing structured sets of parameters  50%-75% sparsity rate
  Unstructured: Arbitrary patterns of sparsification for parameters  90% sparsity rate
Attention pruning (Sparse attention)
  Unstructured attention score: Keep the Top-k largest attention score activations
  Row-wise structured: Load the corresponding rows of the Value matrix from HBM endpoints
Fine-Grained Sparsification

## Slide 12: QuantSparse3D: Advanced Integration
  Advanced integration technology creates heterogeneous tiers that require both accurate architectural modeling and compiler support for tier-aware scheduling and fast DSE
Traditional CMOS scaling approaches its limits
  2.5D Packaging: Multiple active semiconductor dies are placed side-by-side on an interposer
  3D Integration: Stacking multiple active semiconductor dies on top of each other
Challenges:
  Modern AI compilers are designed for static 2D architectures. AI compilers must match computation and memory characteristics to the heterogeneity across the 3D system
  Lack of architectural models of 3D-integrated systems for fast DSE
AMD Instinct MI350
Moving Forward: 3.5D Integration, CMOS 2.0
SI Interposer
XCD
Cache
HBM
Heterogeneous, layer-specialized 3D integration
Fine-pitch HB
Double-sided processing
3D Modeling and Multi-Node DSE Framework

## Slide 13: Baseline Architecture: SoftHier
SoftHier Architecture
  System Level
    Clusters in 2D-Mesh, HBM as main memory
    Clusters and HBM CTRL connected by NoC
  Compute Cluster
    Vector, Tensor Compute Engines
    Snitch – RISC-V Core
    TCDM Multi-banked L1
    iDMA Engine
GVSoC: Fast and Accurate System-level Simulator
  Block-level model integration; calibrate using RTL findings
  Provide accurate timing* and fast simulation**
  Use GVSoC to evaluate architectural design with end-to-end applications at fast simulation rate
Core 0
Core 0
…
Core n
Comp. Engine
iDMA
I $
TCDM (Multi-banked L1)
CTRL
REG
Interconnect
To Data NoC Router
To Sync NoC Router
Cluster
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
HBM
HBM
HBM
HBM
R
R
Data NoC Router
Sync NoC Router
* Accurate timing: <10% runtime deviation vs. FPGA emulation of PULP Ips ** Fast simulation: 25 MIPS measured with a 16-core PULP Cluster
Notes: naming

## Slide 14: Compute Engine Considerations
ML models are updated on a weekly basis
Model sparsification and quantization promise substantial efficiency gains
Rapid evolution demands that hardware can adapt fast
NVIDIA Sparse Tensor Core
Support mapping 2:4 structured sparsity format
MicroScopiQ[1]
WS systolic array for outlier-aware quantization
  Bulky Accelerators
  Format rigidity, Low reusability, Underutilization in inference
Research trends:
  FPGA, CGRA-based Designs
  Offer programmability but at the cost of energy efficiency
Onxy[2]
Programmable accelerator for sparse tensor algebra
  We need configurable specialization to bridge HW flexibility and efficiency
Opal[3]
CGRA for Full Sparse Machine Learning
[1] R. Akshat, et al. "Microscopiq: Accelerating foundational models through outlier-aware microscaling quantization." ISCA ‘25.
[2] K. Kalhan, et al. "Onyx: A 12nm 756 GOPS/W coarse-grained reconfigurable array for accelerating dense and sparse applications." VLSI ‘24.
[3] K. Jahyun, et al. "OPAL: Outlier-Preserved Microscaling Quantization Accelerator for Generative Large Language Models." DAC ‘24.
Native HW Acceleration for Model Compression

## Slide 15: Vector Processor as the Main Compute Engine
Vector engine
  Computation speedup on vectorizable operations
   improved energy efficiency w.r.t scalar cores
  Compatible with vector-level operations and multi-granularity sparsity (structured and indexed)
+ Matrix ISA extensions
  Arm SME[1], Intel AMX[2], and IBM MMA[3]
  Direct handling of matrix operations  lowering the instruction fetch and setup overhead
  Minimizes the bandwidth demand between VRF and the VAUs  reduced energy consumption

## Slide 16: Proposed Architecture
  Efficient scatter/gather unit
  Structured Sparsity in Cluster
  Indirect streaming + scatter/gather unit
  Unstructured Sparsity in Cluster
  Gather from HBM endpoint
  Unstructured Sparsity in NoC
  Customized MX-format in Vec. Engine
  Block Quantization
  Router with additional degrees of freedom
  3D Architectural Modeling
Notes: naming

## Slide 17: Proposed Architecture
  Efficient scatter/gather unit
  Structured Sparsity in Cluster
  Indirect streaming + scatter/gather unit
  Unstructured Sparsity in Cluster
  Gather from HBM endpoint
  Unstructured Sparsity in NoC
  Customized MX-format in Vec. Engine
  Block Quantization
  Router with additional degrees of freedom
  3D Architectural Modeling
Notes: naming

## Slide 18: Handling MX Format in the Scalar Processor
MXDOTP operation group
  Datapath is integrated into the FPU of the Snitch Cluster as an additional operation group
  Computes the dot product between vectors of eight FP8 elements
  Throughput: one FP32 result per cycle
Implementation and area analysis
  Synthesize, PnR with GF 12nm FinFET
  1.09GHz @ TT/0.8V/25°C, with three pipeline stages, without introducing new critical paths
  26 kGE per MXDOTP datapath, 17% of FPU area
MXDOTP[1]: RV ISA Extension for MX Dot Products
[1] İslamoğlu, Gamze, et al. "MXDOTP: A RISC-V ISA Extension for Enabling Microscaling (MX) Floating-Point Dot Products." arXiv preprint arXiv:2505.13159 (2025).

## Slide 19: VMXDOTP: Bring MXDOTP Datapath to the Vector Processor
Per FPU workload
Spatz Datapath and Software Emulated MX kernels
Vector processing unit (VPU)
  Comprises four 64-bit FPUs operating in parallel
  Connected via 256-bit interconnects to VREG
Software emulation of MXFP8-MatMul Kernel
  Gustavson’s algorithm: vectorizes computation along the output matrix’s row dimension
  Expend FP8 inputs to FP16, and multiply with widening FMA
  Unscaled dot products and the expanded scales are combined using a vector-vector FMA
Design goals:
  Eliminate the overhead of software scaling and explicit precision conversion
  Must include a fused accumulation step
  Support multiple formats and flexible block size

## Slide 20: VMXDOTP: Spatz Integration
Spatz Integration
  VMXDOTP extension leverages MXDOTP datapath  FPUs in Spatz VPU extended with the MXDOTP operation group
  Preliminary encoding for proof-of-concept experiments
Implementation and area analysis
  Synthesize, PnR with GF 12nm FinFET. 1.27 GHz @ TT/0.8V/25°C, without introducing new critical paths
  Hardware overhead is low:
    VMXDOTP-enabled Spatz cluster has a total area of 4.28 MGE: 12.6 % and 7.2 % increment at CC and cluster level
    The MX dot-product unit accounts for 82% of the incremental area overhead
ISA Extension and PnR Analysis

## Slide 21: VMXDOTP: Spatz Integration
GEMM Dataflow with VMXDOTP
  Activation matrix is row-wise quantized, weight matrix is column-wise quantized
  Per FPU operates on an inner-product dataflow
  Per Spatz operates on a Gustavson’s-based dataflow
GEMM benchmark
  Output dimension: 64x64, sweep the inner dimension from 64 to 512
  High performance gain and energy efficiency:
    ~3.6x, 7.0x speedup at 1.9x, 4.9x energy efficiency comparing with FP32, MXFP8 baseline
    MXFP4 VMXDOTP kernels double the throughput and efficiency of their MXFP8 counterparts
    FPU utilization of 97.6 %
Per Spatz workload
Kernel Implementation and Benchmark

## Slide 22: Proposed Architecture
  Efficient scatter/gather unit
  Structured Sparsity in Cluster
  Indirect streaming + scatter/gather unit
  Unstructured Sparsity in Cluster
  Gather from HBM endpoint
  Unstructured Sparsity in NoC
  Customized MX-format in Vec. Engine
  Block Quantization
  Router with additional degrees of freedom
  3D Architectural Modeling
Notes: naming

## Slide 23: Software Emulation of Structured Sparsity Handling
SpMM Implementation with RVV
Index generation is required
1
1
No VRF scatter RVV support
 Use L1 to accumulate
2
2
2
~50% instructions are used for config + scatter/gather
3
3
Design insights:
  Native hardware support for N:M index formats
  Eliminate configuration overhead for distinct SEW
  Perform scatter/gather operations in VRF

## Slide 24: Widening-indexed MACC Instructions
32x32x1024 SpMM
Scatter/Gather in VRF
Merged index translation
No configuration overhead
Performance detected from the roofline
  Scatter/Gather operation is inefficient  For a 50% sparsity rate, effective VPU throughput is halved
  Worse with higher sparsity rate

## Slide 25: Efficient Scatter/Gather Datapath
Spatz VRF is implemented as a multi-banked, multi-ported, latch-based standard cell memory (SCM)
  32 VLENB bytes of the VRF are divided into four banks
  three read ports and one write port (3R1W)  Provides enough bandwidth for executing vfmacc.vv instruction
  Each with VLENB/2 byte width
In SoftHier, Spatz VLENB = 512 (i.e., 16 KiB VRF)
Spatz has three function units:
  VAU: Vector Arithmetic Unit
  VLSU: Vector Load/Store Unit
  VSLDU: Vector Slides Unit
Spatz VRF Architecture

## Slide 26: Efficient Scatter/Gather Datapath
Extended VSLDU with an additional port for indices
  Support native N:M formats
Limitations:
  Throughput bottleneck: With a 50% sparsity rate, Cycle 1 produces the upper-half gathered output, and Cycle 2 produces the lower-half
  Lack of streaming: VSLDU gathers a vector from VRF, writes it back, and requires an additional read for arithmetic.
Insights on design requirement:
  Asymmetrical bandwidth required to feed VAU at full utilization
  Streamlined Scatter/Gather operation with arithmetic
Existing VSLDU-based design

## Slide 27: Ventaglio: Efficient Scatter/Gather Datapath
Memory unit
  Provide a configurable number of channels (currently 4), each aligned with the VAU datapath granularity
  Configurable number of rows, currently 4 rows per channel to support LMUL=8
  Implemented with arrays of clock-gated flip-flops
Scatter/Gather datapath
  To select the effective elements based on the index vector
  Provides asymmetrical interfaces, connecting memory units and the VAU/VRF interfaces
Scatter/Gather crossbars
  (Load/Store phase) Route the data stream from VLSU directly into the memory units
  (Compute phase) Route the data stream through the scatter/gather datapath

## Slide 28: Ventaglio: Efficient Scatter/Gather Datapath
VSLDU substitution
  VTL is capable of all the functions of VSLDU, exposing the same interface towards VRF
VAU Crossbar
  The gather operation can be applied to both activation and accumulation tensors
    Applied to the accumulation (i.e., with Gustavson’s dataflow), it is written back to the VTL memory units
    With Inner-product-based dataflow (i.e., VMXDOTP), the gather operation is applied to the activation tensor  accumulations are stored back in the VRF
Spatz Integration

## Slide 29: Ventaglio: Efficient Scatter/Gather Datapath
High performance gain
  Achieve 1.9x~6.1x speedup compared with the VSLDU baseline
Still detached from the roofline
  Impacts from: Control instructions for address calculation and explicit scalar activation elements loading
  More prominent with a higher sparsity rate.
Behavioral Modeling and Benchmark
Scalar activation streaming
Address post increment

## Slide 30: Joint Handling of Structured Sparsity and MX
Sparsification-axis Consideration
Orthogonal to the MX blocks
  Columns of weight elements utilize distinct shared scales
  An additional shuffling stage to group elements with the same scales together
  Dynamic MAC unit linkage relies on N:M indices
  Separate logic blocks for applying scales and accumulation
   Difficult to scale for various N:M format and MX precisions

## Slide 31: Joint Handling of Structured Sparsity and MX
Aligned to the MX blocks
  Columns of weight elements share the same MX scales
  An additional gathering stage for effective activation elements (Using VTL)
  MXDOTP datapath remains unchanged
Sparsification-axis Consideration
Orthogonal to the MX blocks
  Columns of weight elements utilize distinct shared scales
  An additional shuffling stage to group elements with the same scales together
  Dynamic MAC unit linkage relies on N:M indices
  Separate logic blocks for applying scales and accumulation
   Difficult to scale for various N:M format and MX precisions

## Slide 32: Proposed Architecture
  Efficient scatter/gather unit
  Structured Sparsity in Cluster
  Indirect streaming + scatter/gather unit
  Unstructured Sparsity in Cluster
  Gather from HBM endpoint
  Unstructured Sparsity in NoC
  Customized MX-format in Vec. Engine
  Block Quantization
  Router with additional degrees of freedom
  3D Architectural Modeling
Notes: naming

## Slide 33: Unstructured Sparsity in Cluster: Target Applications
Unstructured weight matrix pruning
  Sparsity ratio ~10%
  Example methods: OWL[1], Optimal BERT Surgeon[2]
Weight matrix outlier
  From extreme compression scenarios
  Example methods: SpQR[3], SqueezeLLM[4], GPT3.int8()[5]
  Sparsity ratio 0.01-1%
[1] Yin, Lu, et al. "Outlier weighed layerwise sparsity (owl): A missing secret sauce for pruning llms to high sparsity." arXiv preprint arXiv:2310.05175 (2023).
[2] Kurtic, Eldar, et al. "The optimal bert surgeon: Scalable and accurate second-order pruning for large language models." arXiv preprint arXiv:2203.07259 (2022).
[3] Dettmers, Tim, et al. "Spqr: A sparse-quantized representation for near-lossless llm weight compression." arXiv preprint arXiv:2306.03078 (2023).
[4] Kim, Sehoon, et al. "Squeezellm: Dense-and-sparse quantization." arXiv preprint arXiv:2306.07629 (2023).
[5] Dettmers, Tim, et al. "Gpt3. int8 (): 8-bit matrix multiplication for transformers at scale." Advances in neural information processing systems 35 (2022): 30318-30332.

## Slide 34: Occamy: Unstructured Sparsity handling with SUs
Streaming units(SU) maximize FPU utilization
  Eliminating the control overheads of streaming SPM accesses
  Map streams of SPM accesses directly to FP registers, support:
    4-D strided accesses
    Indirect streams with 8-, 16-, or 32-bit indices
    Indices comparison for tensor intersection/union
SUs enable a sustained core-SPM bandwidth
  FPU utilization is no longer bound by control overheads  bound by SPM’s throughput
In Scalar Cores

## Slide 35: Handle Unstructured Sparsity in Vector Processor
ELLPACK format
  Compresses an N×P matrix into two K×P matrices for effective values and row indices
  K is the maximum number of non-zero elements per column.
  Well-suited for vector-level processing, provided that the number of non-zeros per matrix column does not vary signiﬁcantly
Compress direction
ELLPACK Format

## Slide 36: Handle Unstructured Sparsity in Vector Processor
SpMV with ELLPACK format
  Each output element results from the reduction between the activation vector and a column of the weight matrix.
  Two dataflows are available; Gustavson’s dataflow is preferred
  Row indices are used for RVV index-load operation
Kernel Implementation with ELLPACK Format

## Slide 37: Case Study: Outliers from SpQR[3] Method
Reproduced on the Llama-2-7B model
  Performed a per-layer analysis
  Evident outlier patterns:
    Attention head patterns: Some heads (e.g., head 0 in this example) contain significantly more outliers.
    Row-wise patterns: Corresponding to subsets of output features.
    Column-wise patterns: Corresponding to subsets of input features.
  Observation:
    The number of outliers per matrix row/column vary signiﬁcantly
Layer_0: o_proj
Attention head pattern
Row-wise patterns
Column-wise pattern

## Slide 38: Case Study: Outliers from SpQR[3] Method
Layer_0: o_proj
Compressed
Direction
Well-captured column-wise and attention head patterns
Spiking
Row patterns
Limitation of ELLPACK Format
Key challenge: Spiking row patterns
  A few rows contain an unusually high number of outliers  a large amount of zero-padding in the ELLPACK value matrix.
Multi-level ELLPACK Format

## Slide 39: Multi-Level ELLPACK Format
Dynamic compression technique
  Fully offline, served as an extension for the existing quantization framework
    Dynamic threshold based on weight matrix profiling
    Additional overhead: Keep a small column indices vector
Removing Zero Padding Through Two-Level Compression

## Slide 40: Multi-Level ELLPACK Format
Example: SpMV Kernel Implementation

## Slide 41: Multi-Level ELLPACK Format
Example: SpMV Kernel Implementation

## Slide 42: Multi-Level ELLPACK Format
Example: SpMV Kernel Implementation

## Slide 43: Ventaglio: Two-Level Gather Mechanism
Example: 32-bit datapath, 32-bit bank width; FP16 outliers
Block size = L1 Bank width
 2 elements per block

## Slide 44: Ventaglio: Two-Level Gather Mechanism
Example: 32-bit datapath, 32-bit bank width; FP16 outliers
Block size = L1 Bank width
 2 elements per block

## Slide 45: Ventaglio: Two-Level Gather Mechanism
Example: 32-bit datapath, 32-bit bank width; FP16 outliers
Block size = L1 Bank width
 2 elements per block

## Slide 46: Proposed Architecture
  Efficient scatter/gather unit
  Structured Sparsity in Cluster
  Indirect streaming + scatter/gather unit
  Unstructured Sparsity in Cluster
  Gather from HBM endpoint
  Unstructured Sparsity in NoC
  Customized MX-format in Vec. Engine
  Block Quantization
  Router with additional degrees of freedom
  3D Architectural Modeling
Notes: naming

## Slide 47
Decode: sparse (e.g. top-k) attention gathers vectors from V cache
  V cache is in HBM, cannot fit in SPM
  Entries may be as narrow as NoC bus (Llama-3: h=128 @ 4b  512b)
V-Cache Gather for Sparse Attention
sparse attn. a
V
V cache
a1
a3
a4
as
0
0
0
0
v1
v3
v4
vs
output z
gathered V_vecs
Cluster tile
TCDM (Multi-banked L1)
iDMA
a_idcs
V_vecs
DMA control core
gather(a_idcs, V_vecs)
req. gen
NoC NI + Router
response writeback
NoC Mesh
HBM Endp. 0
Ctrl.
HBM Endp. 1
Ctrl.
HBM Endp. 2
Ctrl.
HBM Endp. 3
Ctrl.
Req 0: E1
Req 1: E0
Req 2: E1
Req 3: E1
Req 4: E2
Req 5: E3
Indices

## Slide 48
Decode: sparse (e.g. top-k) attention gathers vectors from V cache
  V cache is in HBM, cannot fit in SPM
  Entries may be as narrow as NoC bus (Llama-3: h=128 @ 4b  512b)
  Benefits from efficient mechanism to gather short vectors from HBM
V-Cache Gather for Sparse Attention
sparse attn. a
V
V cache
a1
a3
a4
as
0
0
0
0
v1
v3
v4
vs
output z
gathered V_vecs
Cluster tile
TCDM (Multi-banked L1)
iDMA
a_idcs
V_vecs
DMA control core
gather(a_idcs, V_vecs)
req. gen
NoC NI + Router
response writeback
NoC Mesh
HBM Endp. 0
Ctrl.
HBM Endp. 1
Ctrl.
HBM Endp. 2
Ctrl.
HBM Endp. 3
Ctrl.
Rsp 1: E0
Rsp 3: E1
Rsp 4: E2
Rsp 5: E3
Rsp 2: E1
Rsp 0: E1

## Slide 49
Decode: sparse (e.g. top-k) attention gathers vectors from V cache
  V cache is in HBM, cannot fit in SPM
  Entries may be as narrow as NoC bus (Llama-3: h=128 @ 4b  512b)
  Benefits from efficient mechanism to gather short vectors from HBM
Extend cluster DMA with indexed gather
  Read selected attention indices from cluster TCDM
  Collect, pack requests per HBM endpoint
V-Cache Gather for Sparse Attention
sparse attn. a
V
V cache
a1
a3
a4
as
0
0
0
0
v1
v3
v4
vs
output z
gathered V_vecs
Cluster tile
TCDM (Multi-banked L1)
iDMA
a_idcs
V_vecs
DMA control core
gather(a_idcs, V_vecs)
req. gen
endpoint packing
NoC NI + Router
wb info
response writeback
NoC Mesh
HBM Endp. 0
gather burst handler
Ctrl.
HBM Endp. 1
HBM Endp. 2
HBM Endp. N
Req
size=6
Indices
Req 5
size=1
Req 4
size=1
Req 1
size=1
Req 0, 2, 3
size=3

## Slide 50
Decode: sparse (e.g. top-k) attention gathers vectors from V cache
  V cache is in HBM, cannot fit in SPM
  Entries may be as narrow as NoC bus (Llama-3: h=128 @ 4b  512b)
  Benefits from efficient mechanism to gather short vectors from HBM
Extend cluster DMA with indexed gather
  Read selected attention indices from cluster TCDM
  Collect, pack requests per HBM endpoint
  HBM endpoints send back packed bursts of needed V-cache vectors
  Increased bandwidth efficiency
V-Cache Gather for Sparse Attention
sparse attn. a
V
V cache
a1
a3
a4
as
0
0
0
0
v1
v3
v4
vs
output z
gathered V_vecs
Cluster tile
TCDM (Multi-banked L1)
iDMA
a_idcs
V_vecs
DMA control core
gather(a_idcs, V_vecs)
req. gen
endpoint packing
NoC NI + Router
wb info
response writeback
NoC Mesh
HBM Endp. 0
gather burst handler
Ctrl.
HBM Endp. 1
HBM Endp. 2
HBM Endp. N
Rsp 5
size=1
Rsp 4
size=1
Rsp 1
size=1
Rsp 0, 2, 3
size=3

## Slide 51: Proposed Architecture
  Efficient scatter/gather unit
  Structured Sparsity in Cluster
  Indirect streaming + scatter/gather unit
  Unstructured Sparsity in Cluster
  Gather from HBM endpoint
  Unstructured Sparsity in NoC
  Customized MX-format in Vec. Engine
  Block Quantization
  Router with additional degrees of freedom
  3D Architectural Modeling
Notes: naming

## Slide 52
Minimize the network diameter
  Why: fewer hops → fewer routers involved per packet → lower latency, lower congestion, lower energy
Tune the link range
  Shorter links → higher signaling rate (i.e., lower RC).
  Trade-off: shorter links require more routers to maintain reachability, thus a larger network diameter
Optimize the Router Radix
  Higher radix  smaller network diameter
  Trade-off: Higher radix increases area, buffering, crossbar size, and control complexity
Key insight:
  Lowering the network diameter often requires increasing the radix, but the area/bandwidth trade-off must be modeled.
3D Router Modeling
Design Principles for Inter-Chiplet/Inter-Cluster Interconnect Topology

## Slide 53
Design goals:
  Extend the router model with 3D-aware degrees of freedom to capture:
    Vertical vs. lateral link allocation
    Hybrid 2.5D–3D topologies
    Variable link lengths and link-quality scaling
  Capture the quantitative trade-off between router radix, area overhead, and per-port bandwidth.
  Model how link range and network diameter co-determine latency, congestion, and throughput.
3D router modeling baseline
  Adding two degrees of freedom along the Z-dimension
  Defining the lower bound on routing distance and network diameter
3D Router Modeling
Design Principles for Inter-Chiplet/Inter-Cluster Interconnect Topology

## Slide 54: Proposed Architecture
  Efficient scatter/gather unit
  Structured Sparsity in Cluster
  Indirect streaming + scatter/gather unit
  Unstructured Sparsity in Cluster
  Gather from HBM endpoint
  Unstructured Sparsity in NoC
  Customized MX-format in Vec. Engine
  Block Quantization
  Router with additional degrees of freedom
  3D Architectural Modeling
Notes: naming

## Slide 55: Review of First-Year Work Package
(WP1.1) Architectural modeling, simulation, and design of the chiplet architecture
  [Done] Modeled (widened) indexed-macc in the vector processor Spatz for sparsity handling
  [Done] Modeled vmxdotp instructions in Spatz for block quantization data format handling
  [Done] Modeled on-chip interconnect, memories, and main memory endpoints.
  [Finishing] Modeled controller and collecting packets in the main memory endpoint
(WP1.2) Parameterized RTL models
  [Done] MXDOTP operation group has been integrated into Spatz. It is synthesized with the GF12 technology node and performs PPA analysis.
  [Done] RTL implementation of controller in main memory endpoint
  [Ongoing] The Ventaglio gather and scatter datapath is being integrated into Spatz. – Expect to finish in November (M9)

## Slide 56: Review of First-Year Work Package
(WP2.1) Architectural modeling of 3D-stacked memories
  [Finishing] Extend the router model with optional 3D (z-up and z-down) routing – Expect to finish in November (M9)
(WP2.2) Software environment for LLM Deployment
  [Done] Extended SoftHier runtime with dynamic memory allocation in both L1 SPM and HBM.
  [Done] Integrated the SoftHier runtime and basic kernel templates into the Deeploy framework. Achieved single-cluster microkernel deployment.
  [Ongoing] Extending the deployment framework to support multi-node architectures. – Expect to finish in January (M11)
(WP2.3) DSE for simplified end-to-end models and microkernels
  [Done] Implemented microkernels for SpMM and SpMV kernels with structured sparse weight matrix and unstructured activations. GEMM and GEMV kernels with MX block quantization format.
  [Ongoing] Proposed multi-level ELLPACK format for SpMV kernel with unstructured sparse weight matrix. HW-SW co-design with Ventaglio scatter/gather datapath. – Expect to finish in December (M10)
  [Pending] Implementation of end-to-end model deployment. – Expect to finish in February (M12)

## Slide 57: Ventaglio: Efficient Scatter/Gather Datapath
Loading stage
  Vector of activation elements is loaded from L1 through VLSU, and written to the memory units in VTL  bypassing VRF
Example: Inner-Product Dataflow

## Slide 58: Ventaglio: Efficient Scatter/Gather Datapath
Loading stage
  Vector of activation elements is loaded from L1 through VLSU, and written to the memory units in VTL  bypassing VRF
Compute stage
  Effective activation elements are gathered with indices
  The vector of weight elements and output accumulations are streamed from VRF
  Decoupled loading stage and compute stage
Example: Inner-Product Dataflow

## Slide 59: Ventaglio – Spatz Integration
Gustavson’s dataflow example
  Vector of weight elements is streamed from VRF (rs1)
  Scalar activation elements are read from scalar registers
  Vector of output accumulations is gathered-read from VTL, and scattered-write back to VTL
  Indices are read from the VRF