## Slide 1: QuantSparse 3D Biweekly 2025-12-18
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  Ventaglio – Scatter and gather datapath
  3D architectural modeling
Timeline
Discussion

## Slide 3: Spatz Requests Processing
Spatz controller
  Maintains a scoreboard to track instruction dependencies
  Resolves dependencies between Spatz instructions
  Manages instruction issuing and retirement
    Upon receiving an offload request from Snitch: Decode the request; Enrich it with additional metadata to form a Spatz request
    Check the scoreboard: Register the instruction as in-flight; Update dependency state
    Broadcast the Spatz request to all downstream units
Spatz function units
  Filter incoming Spatz requests based on matching ex_unit
  Process eligible requests
  Each function unit exposes multiple memory master ports to the VRF

## Slide 4: Streamline Scatter/Gather Operations
Bypassing VRF
  Operands involved in scatter/gather operations should be accessed directly by the VPU, bypassing the VRF
  High-level architectural changes
    VTL: 1. Add an additional memory slave port (1R/1W)
    Controller: 1. Introduce a VTL table to decide whether a memory request should bypass the VRF. (We configure a vector register that is mapped to the VTL memory unit) 2. Attach VTL metadata to the Spatz request when bypassing is enabled
    VRF: 1. Add one memory master port (1R/1W) 2. Forward selected memory requests to VTL 3. Enable VLSU-generated memory requests to bypass the VRF Vector load/store instructions can access VTL memory units directly

## Slide 5: Custom Instructions
Vector load index (vlx.v vd)
  Reuse a vacant VRF slot to store index vectors
  Index element bitwidth is configured ahead of execution  No need to specify SEW in the instruction
  Vector length vl for the load/store is inferred by the controller
  The VTL table always maps vd to the VRF
Indexed MACC operation (vfxmacc.vf vd, rs1, vs2)
  The index vector implicitly shares the same VID as the vector register mapped to VTL  Enables non-intrusive instruction encoding
  The controller attaches VTL metadata to enable bypass, gather, and scatter logic
  The generated Spatz request is also captured by VTL
  No changes required in the VPU. Still executes standard vfmacc operations.

## Slide 6: VTL Implementation
Memory Slave Port (Data Side)
  Vector load/store instructions bypass the scatter/gather datapath  Access memory units directly
  vfxmacc instruction enables the scatter/gather datapath  Supplies effective elements to the VPU
Memory Master Port (Index Side)
  Read index vectors from the corresponding VRF slots
  Due to bitwidth mismatch, the master read port operates at a much lower frequency
  Index readback is buffered in a VLEN-bit index buffer
Address Generation & Scheduling
  Coupled with a beat counter. Prefetches indices ahead of data consumption

## Slide 7: Example Walk Through
set_vtl
vlx.v
vle.v
vfxmacc
idx
vse.v
w

## Slide 8: Example Walk Through
idx
vse.v
w
acc
idx
acc

## Slide 9: Example Walk Through
idx
vse.v
acc
idx
acc

## Slide 10: Example Walk Through
idx
vse.v
acc

## Slide 11: Example Walk Through
idx
acc

## Slide 12: Current Progress
First version RTL finished
  Ventaglio is integrated in Spatz
  Currently supports 2:4 format; more formats will be supported soon
  Custom instructions functional verification done
Baseline SpMV kernel implementation done
  Benchmark and performance analysis are ongoing

## Slide 13: 3D Architectural Modeling: NoC Extension
Extended FlooNoC model with z-axis routing
  Fully parametric, backward-compatible
  For axis-ordered routing: Z first
  Verified in vanilla GVSoC
Currently: Implementing additional collectives features from SoftHier in 3D
Next: Explore heterogeneous 3D links, different inter-die topologies
  Different Z throughput and bandwidth
  Higher Z arity (more links)
  Different Z connection topologies
R
R
R
R
R
logic die
logic die
...
...