## Slide 1: QuantSparse 3D Biweekly 2026-03-26
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch
Chi Zhang chizhang@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  Ventaglio – GVSoC modeling and calibration; E2E framework adaptation
  3D System – Discussion on the plan to model flexible 3D NoC
Timeline
Discussion

## Slide 3: Recap: Ventaglio
Finished Ventaglio RTL implementation and kernel development
  Post-increment extension for vector load instructions;
  Updated SpMM and SpMV kernels; finished kernel benchmarks; achieved at-the-roofline performance;
  All custom instructions have LLVM and RISC-V opcodes supports.
New project launched
  SA – Integrating Ventaglio with VMXDOTP
    Inner-product dataflow; Bitmap indices for MX-blocks
Next step:
  Started Ventaglio modeling and calibration  E2E benchmark

## Slide 4: Ventaglio E2E Simulation on SoftHier
Spatz modeling in GVSoC
  Ported the baseline FP32 and FP16 GEMM/GEMV kernels from RTL benchmark to GVSoC
  Implemented HBM preload mode for testing arbitrarily large matrix size
Ventaglio instruction modeling in GVSoC
  Added 3 sets of new instructions with index semantics to Spatz GVSoC ISS decoder
    vlx*.v, vfxmacc.vf, and vfxmul.vf, with timing annotation
  Added post-increment extension instructions
  Calibrated against SpMM/SpMV kernels RTL simulation across 8 problem sizes
    Mx16x16 – Mx128x128, for both 2:4 and 1:4 sparsity formats
    With maximum 2.3% error
SUMMA dataflow integration:
  Implemented SUMMA-based Spatz GEMM/SpMM kernels
    Drop-in replacement for the RedMuLE SummaGEMM
    Adapted sparse-aware DMA

## Slide 5: Ventaglio E2E Simulation on SoftHier
Work in progress
  Spatz SUMMA optimizer: L1 capacity constraint for double-buffered tiling and dataflow
  Adaptation to GEMV/SpMV for autoregressive decoding
Next step
  E2E pipeline integration: Add Spatz-base SUMMA implementations to the flow pipeline
  3-way comparison (dense, 2:4 sparse, and 1:4 sparse) on Qwen-7B