## Slide 1: QuantSparse 3D Biweekly 2025-10-30 Pre-Discussion on Stage Report
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Progress Recap
  WP1
  Proposal for the unstructured SpMV dataflow and custom ELLPACK data format

## Slide 3: Agenda
Progress Update
  Ventaglio – Scatter and gather datapath
  Pre-discussion on the stage report
    Work package revisit
    Proposed structure of stage report
Timeline
Discussion

## Slide 4: Ventaglio – Scatter/Gather Datapath
Memory unit
  Configurable number of rows, currently 4 rows per channel to support LMUL=8
  Currently implemented with arrays of clock-gated flip-flops
Scatter/Gather datapath
  To select the effective elements based on the index vector
  Provides symmetrical interfaces

## Slide 5: Ventaglio – Scatter/Gather Datapath
Gather/Scatter crossbars
  Actively switching connections  (Load/Store phase) Route the data stream from VLSU directly into the memory units (Compute phase) Route the data stream through the scatter/gather datapath

## Slide 6: Ventaglio – Spatz Integration
VSLDU substitution
  VTL is capable of all the functions of VSLDU, exposing the same interface towards VRF
VAU Crossbar
  The gather operation can be applied to both activation and accumulation tensors
  If gather and scatter are applied to the accumulation (i.e., with Gustavson’s dataflow), it is written back to the VTL memory units
  With mixed, Inner-product-based dataflow, the gather operation is only applied to the activation tensor  accumulations are stored back in the VRF

## Slide 7: Ventaglio – Spatz Integration
Gustavson’s dataflow example
  Vector of weight elements is streamed from VRF (rs1)
  Scalar activation elements are read from scalar registers
  Vector of output accumulations is gathered-read from VTL, and scattered-write back to VTL
  Indices are read from the VRF

## Slide 8: Ventaglio – Spatz Integration
Mixed- inner-product dataflow example
  Vector of activation elements is loaded from L1 through VLSU, and written to the memory units in VTL  bypassing VRF

## Slide 9: Ventaglio – Spatz Integration
Mixed- inner-product dataflow example
  Vector of activation elements is loaded from L1 through VLSU, and written to the memory units in VTL  bypassing VRF
Compute stage
  Effective activation elements are gathered with indices
  The vector of weight elements and output accumulations are streamed from VRF

## Slide 10: Review of First-Year Work Package
(WP1) Chiplet architecture and building blocks
  Architectural modeling, simulation, and design of the chiplet architecture, including processing engines, on-chip interconnect, memories, and main memory endpoints (controllers and near/in memory compute units).
  Parameterized RTL models will be built and synthesized on advanced technology models representative of state-of-the-art technologies to assess PPA.
(WP2) System and software design
  Architectural modeling of multi-chiplet fabrics and 3D-stacked memories.
  Software environment for mapping LLM models to the hardware architecture, leveraging open-source environments (PyTorch, TVM, LLVM) and open specifications (ONNX).
  Design space exploration of system configurations using a set of simplified end-to-end models and microkernels, such as autoregressive inference using a KV-cache for long input sequences, also using micro-scaling formats to reduce memory and energy footprints.

## Slide 11: Review of First-Year Work Package
(WP1.1) Architectural modeling, simulation, and design of the chiplet architecture
  [Done] Modeled (widened) indexed-macc in the vector processor Spatz for sparsity handling
  [Done] Modeled vmxdotp instructions in Spatz for block quantization data format handling
  [Done] Modeled on-chip interconnect, memories, and main memory endpoints.
  [Finishing] Modeled controller and coalescer in main memory endpoint
(WP1.2) Parameterized RTL models
  [Done] MXDOTP operation group has been integrated into Spatz. It is synthesized with the GF12 technology node and performs PPA analysis.
  [Done] RTL implementation of controller and coalescer in main memory endpoint
  [Ongoing] The Ventaglio gather and scatter datapath is being integrated into Spatz. – Expect to finish in November (M9)

## Slide 12: Review of First-Year Work Package
(WP2.1) Architectural modeling of 3D-stacked memories
  [Ongoing] Extend the router model with optional 3D (z-up and z-down) routing – Expect to finish in December (M10)
(WP2.2) Software environment for LLM Deployment
  [Done] Extended SoftHier runtime with dynamic memory allocation in both L1 SPM and HBM.
  [Done] Integrated the SoftHier runtime and basic kernel templates into the Deeploy framework. Achieved single-cluster microkernel deployment.
  [Ongoing] Extending the deployment framework to support multi-node architectures. – Expect to finish in January (M11)
(WP2.3) DSE for simplified end-to-end models and microkernels
  [Done] Implemented microkernels for SpMM and SpMV kernels with structured sparse weight matrix and unstructured activations. GEMM and GEMV kernels with MX block quantization format.
  [Ongoing] Proposed multi-level ELLPACK format for SpMV kernel with unstructured sparse weight matrix. HW-SW co-design with Ventaglio scatter/gather datapath. – Expect to finish in December (M10)
  [Pending] Implementation of end-to-end model deployment. – Expect to finish in February (M12)

## Slide 13: Progress Update
  WP1
  Pre-discussion for Stage Report